## Slide 1: Magnetic Resonance Imaging
Introduction to the physical principles of MRI

## Slide 2: Organization
Meet the lecturer
N. Jon Shah
n.j.shah@fz-juelich.de
During the breaks. Anytime by email!

## Slide 3: Organization
For your self studies:
  E.M. Haacke et al, Magnetic Resonance Imaging: Physical Principles and Sequence Design, John Wiley 1999
  Z.P. Liang, P.C. Lauterbur, Principles of Magnetic Resonance Imaging: A Signal Processing Perspective, SPIE 1999
  M.T. Vlaardingerbroek, J.A. den Boer, Magnetic Resonance Imaging: Theory and Practice, Springer, 2003
  J.P. Hornak, Ph.D., The Basics of MRI,
  http://www.cis.rit.edu/htbooks/mri/
Lecture materials:
  Slides, and other information in the virtual learning room (L2P):
  http://www.elearning.rwth-aachen.de
  Login using your student account
  Registration in CAMPUS office for this course is necessary:
    e.g.: CAMPUS > Dozentensuche „Shah“
    => Lehrveranstaltungen
    => Experimentelle Magnetresonanztomographie

## Slide 4: Course Overview
Introduction and Overview
Math Basics
MR Fundamentals
Excitation
Imaging Principles
Sequences and Contrasts
Rapid Imaging
Parallel Imaging
Hardware
Selected Applications

## Slide 5: Outline
Introduction
  Magnetic Resonance Imaging
  Appetiser – some Examples
MR Scanner Components
Physical Introduction
  Spin ½ in B0
  Larmor Precession
  Resonance (excitation and signal reception)
  Relaxation
  FID, Echoes and Fourier Transform
  Basic Idea of MR Imaging
Basic Safety Issues
Sum-up

## Slide 6: MRI ≠ X-ray
Ionizing Radiation
EM absorbtion in the human body:
Frequency (Energy)
100 %
visible light
X-ray
radio waves
( MRI ! )

## Slide 7: Magnetic Resonance Imaging
MRI is a tomography method but it is very different from CT (Computer Tomography)!
Some positive characteristics of MRI:
Non-ionising | Using radio-waves, not X-rays
Non-invasive | No contrast agents required
Soft-tissue sensitive | MRI signal ~ Proton density ρ ~ H2O
Quantitative | MRI signal ~ Magnetisation = f(ρ,T1, T2, T2*, D, α, …)  density, relaxometry, diffusivity, perfusion, …
Multi-contrast | Various imaging sequences/ parameters
Multi-purpose/modal | Anatomy, activity, connectivity, vessels, …
Oblique slices | Flexible spatial encoding with arbitrary image slice orientation.
MRI’s weakness:
low signal-to-noise ratio and usual MRI not usable for material with little water content!

## Slide 8: Discovery of NMR and MRI
Nuclear spin manipulation through external fields:
Static magnetic field: B0·ez  spin polarization
Radiofreq. field: B1(t) ·exy  resonance signal
Paul Lauterbur and Sir Peter Mansfield
Edward Purcell
Gradient field: (G(t)·r) ·ez  spatial frequencies
                 Imaging!
Notes: Bloch & Purcell: Entdecker der nuklearen Magnetresonanz (1945) -> Nobelpreis Physik
Lauterbur & Mansfield: Entdecker der Bildgebung mit Feldgradienten ->Nobelpreis Medizin

## Slide 9: Examples: Multi-Contrast (T1/T2-weighting)

## Slide 10: Examples: Quantitative – Watermap
(Fabian Keil)
100%
0%

## Slide 11: Examples: Perfusion/ Vessels (Angiography)

## Slide 12: Examples: Metabolism (23Na-Imaging)
(Sandro Romanzetti)

## Slide 13: Examples: Connectivity/ Fibres (DTI)
Rüdiger Stirnberg
DTI

## Slide 14: Examples: Function/ Activity (fMRI)
http://www.radiologie.ruhr-uni-bochum.de/imperia/md/images/institut/mrt/fmri.jpg

## Slide 15: Examples: inner volume excitation

## Slide 16: Outline
Introduction
  Magnetic Resonance Imaging
  Appetiser – some Examples
MR Scanner Components
Physical Introduction
  Spin ½ in B0
  Larmor Precession
  Resonance (excitation and signal reception)
  Relaxation
  FID, Echoes and Fourier Transform
  Basic Idea of MR Imaging
Basic Safety Issues
Sum-up

## Slide 17: MR Scanner Components (simplified)
Master Controller
Gradient
Controller
RF
Controller
x
y
z
RF coil
x
z
y
Gradient
coils
Superconducting magnet
(high static field)
Amps
Transmit Amp
Image Reconstruction
Receive Amp
z
x
y
3 Types of magnetic fields:
Static field (B0 ║ z)
Dynamic gradients (Gi = dBz/dri)
Radio-frequency (B1 ┴ z)

## Slide 18: MR Scanner Components (simplified)
3 Types of magnetic fields:
Static field (B0 ║ z)
Dynamic gradients (Gi = dBz/dri)
Radio-frequency (B1 ┴ z)
RF coil
x
z
y
Gradient
coils
Superconducting magnet
(high static field)

## Slide 19: Outline
Introduction
  Magnetic Resonance Imaging
  Appetiser – some Examples
MR Scanner Components
Physical Introduction
  Spin ½ in B0
  Larmor Precession
  Resonance (excitation and signal reception)
  Relaxation
  FID, Echoes and Fourier Transform
  Basic Idea of MR Imaging
Basic Safety Issues
Sum-up

## Slide 20: Nuclear Spin – Basic overview
Atomic nuclei are composed of protons and neutrons that have the quantum mechanical (QM) property of a spin.
Unlike the classical angular momentum the spin is an intrinsic property of elementary particles.
The overall spin of the composed nucleus is called nuclear spin.
The possible values of the spins’ z-component are quantized in integer steps.
= Planck’s constant ≈ 6.626068·10-34 J s
Spin ½ example

## Slide 21: The Proton and Spin 1/2
The most simple atom is Hydrogen, H.
As the human body consists of approx. 70% water, hydrogen is very prevalent.
Hydrogen’s nucleus is only one proton.
Its nuclear spin quantum number is S=½, i.e.
Associated to every nuclear spin is a nuclear magnetic moment,
γ is called the gyromagnetic ratio and is nucleus-specific.
For hydrogen, γ = 267.513·106 rad/(s·T).
42.6 MHz/T

## Slide 22: Nuclear Zeeman Effect
Exposed to a static external magnetic field, B0, the z-components of the nuclear magnetic moments align with B0.
Without loss of generality, the direction of B0 defines the z-axis.
Two possible orientations of the magnetic moments: parallel and anti-parallel with energies
B0≠0
Zeeman splitting
Larmor frequency
B0=0

## Slide 23: Equilibrium Magnetisation
There is a small excess of spins in the lower energy states.
The population fraction is given by Boltzmann statistics
which is a very tiny number at room temperature T.
However, the small excess amounts in a measurable macroscopic magnetisation, M, which is the ensemble average of the nuclear magnetic moments.
The equilibrium magnetisation for N atoms with
nuclear spin quantum number, S, is given by
Curie’s law:
B0≠0
= Boltzmann constant ≈ 1.381·10-23 J / K
M0

## Slide 24: Equilibrium Magnetisation – Example
At B0=1.5T and body temperature, T=310K, the spin excess in the lower energy state amounts only
Since for small x: exp(x) ~ 1 + x, the spin excess in the lower energy state is proportional to the B0 field strength.
B0≠0

## Slide 25: Larmor Precession
B0≠0
Recall that in the equilibrium only the spin’s z-components are aligned with B0.
The transverse components perform circular motion
All spins precess about B0 with the Larmor frequency, ω0!
But the resulting magnetisation is static and aligned with B0!
Nuclear Magnetic Resonance: an EM wave oscillating perpendicular to B0 at Larmor frequency deflects the equilibrium alignment!
the magnetisation precesses about B0 with the Larmor frequency, ω0!
Larmor frequency

## Slide 26: Larmor Precession – Example
At B0=1.5T clinical field strength the Larmor frequency (angular frequency) is
In ordinary frequencies, this corresponds to f0=63.9MHz.
Radiofrequencies!
For 9.4T human research scanner: f0=400MHz!

## Slide 27: Descriptive Derivation of the Larmor Precession
The magnetic field causes a torque, T, on a magnetic moment, μ.
The torque is the 1st derivative of the angular momentum, I, with respect to time.
Ensemble averaging from the microscopic magnetic moments to the macroscopic magnetisation:
Equation of motion* solved by precessional motion with frequency ω=-γB. (clockwise).
* “Bloch-Equation without relaxation”

## Slide 28: Excitation
Apply a resonant radiofrequency (RF) pulse to excite all spins, i.e. excite the macroscopic magnetisation from its equilibrium.
Resonance ↔ frequency of RF pulse = Larmor frequency ω0.
ω0

## Slide 29: MR Signal Reception
t
U [V]
Faraday’s law:
“A changing magnetic flux induces a voltage in a conductive loop.”
(electromotors, dynamos , …)
Maximise the area of the loop by a orienting it perpendicular to the transverse plane (in-plane would cause no voltage at all)

## Slide 30: Relaxation
It is intuitive that equilibrium-magnetisation must be regained somehow.
Heuristically described by two relaxation times:
  T1 (spin-lattice relaxation time)
  T2 (spin-spin relaxation time)
e.g. T1=1000ms
e.g. T2=100ms
T2 ≤ T1 !!!
|M| ≠ const, i.e. funnel-shaped trajectory back to equilibrium

## Slide 31: Classic Treatment of Spin ½ MR: Bloch Equation with Relaxation
Including the relaxation terms, the equation of motion is given by the phenomenological Bloch equation:

## Slide 32: Free Induction Decay (FID)
The received MR signal decays exponentially with the time constant T2.

## Slide 33: The MR Signal Equation
The phase coherence of
determines the signal amplitude:
(r,t0) = const  r  V  |S(t0)| = max
(r,t0) uniquely distributed on [0, 2]  |S(t0)| ≈ 0
  The transverse magnetisation,
  of all magnetization vectors induces the voltage:

## Slide 34: Free Induction Decay (FID), Part II
The received MR signal decays exponentially with the time constant T2.
Local B0 inhomogeneities cause an even shorter effective decay time, T2* (“T-two-star”) through loss of phase coherence:
T2* < T2 !!!

## Slide 35: Spin Echo (SE)
Signal losses due to B0 inhomogeneities is reversible!
Recall a spin echo by inversion of the spins using a 180° pulse.
The individual spin’s phase evolution due to the B0 induced frequency dispersion (T2*) is “rewound”. But T2 decay is irreversible.
90°
180°
Time t
M0
FID ~ exp(-t/T2*)
Spin Echo
Max ~ exp(-TE/T2)
TE
Now, analyse this echo!

## Slide 36: Spin Echo (SE)
Signal losses due to B0 inhomogeneities is reversible!
Recall a spin echo by inversion of the spins using a 180° pulse.
The individual spin’s phase evolution due to the B0 induced frequency dispersion (T2*) is “rewound”. But T2 decay is irreversible.
90°
180°
Time t
M0
FID ~ exp(-t/T2*)
Spin Echo
Max ~ exp(-TE/T2)
TE

## Slide 37: Fourier Transformation (FT)
We expect a frequency dispersion of subgroups of spins – so called isochromats.
That means: most spins precess with the Larmor frequency but some are a little faster and some a little slower.
Obtain spectrum by a Fourier transform (FT) of the time signal, usually a Fast Fourier Transform (performant implementation of a discrete FT)
FFT
Note: the 0.1 kHz proton peak shown in this simplified example would correspond to a very low field strength of B0≈2.3µT according to f0 = ω/ 2π = γB0/2π .
In clinical scanners, the proton frequency ranges between 63.9MHz at 1.5T and 127.7MHz at 3T.
Mx
My

## Slide 38: Fast Fourier Transformation (FFT)
The signal is always demodulated in an analog mixing step before analog to digital conversion (ADC, i.e. digitised sampling of the MR signal).
This demodulation corresponds to moving to another frame of reference, the “rotating frame”.
FFT
In this frame of reference (rotating with the Larmor frequency about z), all resonant spins point to where they were deflected initially.
Mx
My
Mx (demod.)
My (demod.)
Linewidth due to dispersion

## Slide 39: NMR Spectroscopy
Your probe may have protons with a slightly varied precessional frequency.
I.e. the Larmor frequency is influenced by the chemical binding of the protons (“chemical shift”).
Nuclear Magnetic Resonance (NMR) spectroscopy.
FFT
Artificial example with water (Larmor frequency) and a compartment with a 500Hz chemical shift (Larmor frequency + 0.5kHz)
Mx (demod.)
My (demod.)

## Slide 40: Spatial Encoding
The basic idea of MRI:
Make the precessional frequency a function of space!
The “spectrum” then reflects spatial distribution.
Linear field gradients of the B-field in z-direction, e.g. Gx = dBz/dx
B0
G·x
ω0-dω ω0 ω0+dω
x
ω0

## Slide 41: Spin Echo with Frequency Encoding
Take the spin echo and introduce gradients along x.
90°
180°
Time t
M0
TE
Time t
Gx
Spatial dimension, x
~ Protons
Spatial frequency, kx

## Slide 42: Contrast
Different tissues have different T1/T2 times
Generate different contrasts through sequence timing parameters!
90°
180°
Time t
M0
TE
Time t
Gx

## Slide 43: Contrast
Choice of
  Echo time (TE)
  Repetition time (TR)
90°
180°
Time t
90°
180°
90°
180°
90°
180°
TE
TR
TE
TR
TE
TR
TE
TR
…

## Slide 44: Gradient Recalled Echo (SE)
Recall a gradient echo by dephasing and subsequent rephasing in the opposite direction.
Much faster and less RF than spin echo.
But: the individual spin’s phase evolution due to the B0 induced frequency dispersion (T2*) is NOT “rewound”.
90°
Time t
M0
Gradient Echo
Max ~ exp(-TE/T2*)
TE
Time t
Gx

## Slide 45: Imaging Sequences
Gradient encoding must be applied in 3 dimensions for a complete spatial encoding.
  During signal readout: frequency encoding
  In a step-wise procedure (for 1 or more dimensions): phase encoding
  Very common, simultaneous with excitation: slice-selection
Gradients in x, y, and z-direction (dBz/dx, dBz/dy, dBz/dz)
Complex pulse sequences are programmed to obtain all necessary data for a complete reconstruction of the subject. Often: loop-structure.
General goal: fill the “k-space” most quickly.
(image space FFT k-space = FT-coefficients = spatial frequencies).
RF
Gz
Gy
Gx
ADC

## Slide 46: Outline
Introduction
  Magnetic Resonance Imaging
  Appetiser – some Examples
MR Scanner Components
Physical Introduction
  Spin ½ in B0
  Larmor Precession
  Resonance (excitation and signal reception)
  Relaxation
  FID, Echoes and Fourier Transform
  Basic Idea of MR Imaging
Basic Safety Issues
Sum-up

## Slide 47: Basic Safety Issues – The Main Field
Permanently cooled-down (liquid Helium, ~ 4K) superconductor produces the high, static magnetic field B0 ~ 0.1 – 3 Tesla (1T = 10000 Gauss).
Compare: the Earth’s magnetic field on its surface ~ 0.5 Gauss.
Huge force on ferromagnetic material growing rapidly when approaching the magnet.
Objects like a normal fire extinguisher, surgical instruments, tools, keys etc. can cause immense (live-threatening) damage.
Credit cards, cell phones, pacemakers will not work anymore.
Generally, currents are induced in conducting material by changing magnetic flux, e.g. in organs when entering the scanner too quickly (from 0 to B0). Can cause dizziness.

## Slide 48: Basic Safety Issues – Field Gradients
Imaging gradients are ramped up and down repetitively during an imaging sequence.
Max. Amplitude ~ 40 mT/m.
Slew rate is limited to max. 200 mT/(m ms) in order not to stimulate the patient’s peripheral nerves (muscle contraction in arms, back, …)
Patients should not cross their hands in order not to create a conducting loop through their body.
Again, ferro-magnetic parts are not allowed, they would move and cause live-threatening damage.

## Slide 49: Basic Safety Issues – RF fields
High frequency em-waves are emitted to the patient in the order of 100 MHz.
This can lead to hot spots at metallic edges, e.g. cables in contact with the skin or MR-unsafe implants.
Make-up containing metallic particles can heat (also tattoos!)
For higher frequencies the wavelength of the radio-waves inside tissue approaches the extent of, e.g., the head.
High amplitudes due to standing-wave effects.
Amplitude and duration of RF must be controlled due to SAR (Specific Absorption Rate) constraints. SAR is an important issue, particularly at high field strengths because of the reduced wave length.

## Slide 50: Outline
Introduction
  Magnetic Resonance Imaging
  Appetiser – some Examples
MR Scanner Components
Physical Introduction
  Spin ½ in B0
  Larmor Precession
  Resonance (excitation and signal reception)
  Relaxation
  FID, Echoes and Fourier Transform
  Basic Idea of MR Imaging
Basic Safety Issues
Sum-up

## Slide 51: Sum-up
Proton-spins in B0: macroscopic magnetisation (along B0 in equilibrium).
Spins excitable using resonant radio-frequency pulses.
Motion described by Bloch-equation (generally: Larmor precession).
Relaxation described by T1, T2 (and T2*).
MRI acquires echo-signals, usually Spin echoes or Gradient recalled echoes.
A general MRI sequence:
  Excitation (RF pulse)
  Encoding (gradients)
  Data acquisition  FFT  image

## Slide 52: Thank you for your attention
Introduction to MRI