## Slide 1: Elevated concentrations of ethanol in the tunnel and city center of Stuttgart
15.09.2022
Ethanol
© Stuttgart-Marketing GmbH / Werner Dieterich
L. karadurmus, d. klemp, R. Wegener, R. dubus, A.Wahner

## Slide 2
TSU
Tbilisi State University
Prof. Andreas Wahner
Prof. Astrid Kiendler-Scharr
Prof. Bezhan Chankvetadze
Dr. Dieter Klemp
Dr. Robert Wegener
Dr. Franz Rohrer
Dr. Giorgi Jibuti
Rene Dubus

## Slide 3: Motivation
To investigate the composition of volatile organic compounds (VOCs) in the city air of Stuttgart.
To identify causes of these emissions.

## Slide 4
P(O3) aus KW-Abbau
P(O3) aus CO-Abbau P(O3) aus Ethanol-Abbau
 1 O3 pro Molekül CO
 2 O3 pro OH-Angriff
Efficiency of ozone production
 1 O3 pro OH-Angriff
OH + C2H5OH  HO2 + CH3CHO

## Slide 5: introduction

## Slide 6: Literature overview
Literature | Location | Study is based on: | Origins of Ethanol
Dunmore et al. 2016 | UK, London | Measurements | Exhaust and evaporative emissions.
Willey et al. 2019 | USA, NC, Wilmington | Measurements | Production and use of biofuels.
Lewis et al. 2020 | York, UK | Emission Inventory | Solvent use
Gkatzelis et al. 2021 | New York, USA | Measurements | Volatile chemical products (VCPs)

## Slide 7: Experimental approaches
Collection of air samples at different locations in Stuttgart.
Determination of VOC composition and concentration in Stuttgart air samples, using a GC-MS system.
Collection of exhaust emission samples.
Determination of VOC composition and concentration in exhaust gas samples, using a GC-MS system.
Assessment of source contributions by means of CMB analysis.

## Slide 8: Sample collection and analysis systems
Samples were collected in previously evacuated stainless-steel canisters (SILCO-Steel). More than 100 samples collected in several measurement campaigns.
Online measurement of CO2, using Cavity ringdown spectroscopy (CRDS).
Detection limit 2 ppm / 0.1 s

## Slide 9: VOC analysis system
Analysis of the collected VOC samples carried in local laboratory using GC-MS system. Analysis for about 200 individual substances.
Detection limit: 2 - 6 ppt for C2 – C12-VOC

## Slide 10
Math
Chemical Mass Balance (CMB) model
Purpose
To apportion measured pollutant concentrations (or exposures or doses) to their sources, and to assess the proportional contribution of each source.
Math
The CMB receptor model consists of a solution to linear equations that express each receptor chemical concentration as a linear sum of products of source profile abundances and source contributions.
Assumptions
Composition of the source emissions are constant over the period of ambient and source sampling.
Chemical species do not react with each other (i.e. they add linearly).
Notes: The fundamental principle of receptor modeling is based on the assumption that mass is conserved.

## Slide 11
VOC patterns (summer)
μg/m3
μg/m3

## Slide 12
VOC patterns (winter)
μg/m3
μg/m3

## Slide 13: Vehicle exhaust emission profiles
Relative mass fractions
Relative mass fractions

## Slide 14: reactivity distributions of selected fuels
Cold start

## Slide 15
Chart: 
| Tunnel.S | City center.S
Measured VOCmix | 810.3453 | 91.9868
Chart: 
| Tunnel.S | City center.S
Gasoline cold start | 364.3081 | 25.0635
Gasoline warm up phase | 2.4409 | 0.64649
Diesel cold start | 44.3558 | 2.0783
IDLE
Chart: 
| Tunnel.S | City center.S
Measured VOCmix | 810.3453 | 91.9868
Chart: 
| Tunnel.S | City center.S
Gasoline cold start | 483.9647 | 33.825
Gasoline warm up phase | 0 | 0
Diesel cold start | 30.322 | 0.06996
Real Driving
Model results
Tunnel (S)
City (S)
30%
51%
Tunnel (S)
City (S)
37%
64%
μg/m3
μg/m3

## Slide 16
Measured vs calculated masses
Only 12.2 % of measured ethanol emissions are explained by the CMB model
μg/m3
μg/m3

## Slide 17
Measured vs calculated masses
μg/m3
μg/m3
Only 11.8 % of measured ethanol emissions are explained by the CMB model

## Slide 18: Model Results
After adding artificial source of ethanol
Chart: 
| Tunnel.S | City.S
Measured VOCmix | 810.3453 | 91.9868
Chart: 
| Tunnel.S | City.S
Gasoline cold start | 445.8396 | 35.6262
Gasoline warm up phase | 0 | 0
Diesel cold start | 31.8849 | 0
Ethanol | 201.5405 | 14.1269
Tunnel (S)
City (S)
54 %
84 %
μg/m3
Real Driving

## Slide 19: Where ethanol emissions come from?
Ethanol correlates with traffic density

## Slide 20: Where ethanol emissions come from?
Ethanol emissions come from traffic but not from exhaust
Evaporative emissions
Use of Windshield washer fluids

## Slide 21: Evaporative emissions
Ethanol
Parking station VOC patterns
Notes: Ethanol mixing ratio 10 – 60 ppb

## Slide 22: Does evaporation play a role?
Even cold-start gasoline emission profiles can only explain 12% of the measured ethanol.
Ethanol
Cold start gasoline emission profiles

## Slide 23: Ethanol in windshield washer fluids
EU Legislation. Official Journal of the European Union L 99 19.04.2018
“ Methanol Shall not be placed on the market to the general public after 9 May 2018 in windshield washing or defrosting fluids, in a concentration equal to or greater than 0,6 % by weight.“ [1]
[1] Official Journal of the European Union, L 99, 19 April 2018 [EUR-Lex - 32018R0589 - EN - EUR-Lex]
https://eur-lex.europa.eu/legal-content/EN/TXT/PDF/?uri=OJ:L:2018:099:FULL&from=EN
Notes: https://eur-lex.europa.eu/legal-content/EN/TXT/PDF/?uri=OJ:L:2018:102:FULL&from=EN

## Slide 24: Ratio has shifted

## Slide 25: Ethanol content in windscreen washer fluid:
Winter formulations
Summer formulations
Ethanol

## Slide 26: Ethanol content in windscreen washer fluid:
Winter formulations contain ETHANOL.
Summer formulations don’t contain ETHANOL
Ethanol
Windshield washer fluid | Ethanol content [v/v %]
“JET” concentrate -55°C | 45.8 %
“PRIVA” ready mix -60°C | 41.1 %
“ARAL” ready mix -20°C | 26.8 %
38 %

## Slide 27: Ethanol / co2 ratio
Notes: EtOH / CO2 Correlation plot: 1.00E-04 Sweden: 6.20E-04 Finland: 4.20E-04
longer cold seasons seems to be reason of higher ratio

## Slide 28: Ethanol denaturation
 | Ethanol / 2-propanol | Ethanol / MEK
EU Legislation | 3% | 3%
German Legislation | 1% | 1%
“JET” | 1.25% | 0.82%
“Priva” | 1.26% | 0.69%
2-propanol
Methyl Ethyl Ketone
Ethanol

## Slide 29: Ethanol denaturation
 | Ethanol / 2-propanol | Ethanol / MEK
EU Legislation | 3% | 3%
German Legislation | 1% | 1%
“JET” | 1.25% | 0.82%
“Priva” | 1.26% | 0.69%

## Slide 30: Conclusions
Windshield washer fluid can contribute significantly to ethanol emissions in urban areas.
Gasoline cold start dominates the various sources of exhaust emissions for most of the VOCs found on the streets.

## Slide 31: Acknowledgements
GGSB
FZJ (IEK-8)
TSU
BMBF
Valentin Polinowski (FZJ, IEK-8)
Yen-Sen Lu (FZJ, IEK-8)
Wen-Fei Huang (FZJ, IEK-8)
Philip Carlsson (FZJ, IEK-8)
Carl Burket (FZJ, IEK-8)
Anna Noveli (FZJ, IEK-8)
Thank you !

## Slide 32: Ethanol / CO2 ratio
Cars using Windshield fluid | 1 %
Number of cars per day | 50 000
Windshield fluid per injection | 10 mL
Share of Ethanol | 38 %
Total amount of ethanol released / day | 1900 mL
Density | 0.789 g/mol
MW Ethanol | 46 g/mol
Mole Ethanol | 32.59 mol
Gas Volume | 0.795 m3
Tunnel Volume | 5.72E+05 m3
Mixing ratio Ethanol | 1.39 ppm
Average CO2 emission (from HBEFA) | 200 g / km / Vehicle
Total CO2 emitted per day | 23000000 g
MW CO2 | 44 g/mol
Total mols emitted | 522727.27 mol
Gas Volume CO2 | 12754.55 m3
Share CO2 | 2.2 %
Ethanol / CO2 | 6.23E-05
Ethanol / CO2 (from the correlation plot) | 1.00E-04

## Slide 33: Mixing ratios of ethanol
Heslacher Tunnel. Stuttgart. Germany.
Dimensions of Heslacher Tunnel | Traffic frequency
L: 2300m H: 8.9m W: 10.4m | 50 000 vehicles / day
The Heslacher Tunnel is a 2.3 km long two-lane road tunnel in the south of Stuttgart . As part of the federal highway 14 , it is part of the connection from the city center to the Stuttgart motorway junction.
Vtunnel = 5.72E+05 m3
1% of vehicles use windshield washer fluid while driving in the Heslacher Tunnel. 10 mL windshield washer fluid per vehicle. 500 x 10 mL = 5000 mL / day of windshield washer fluid.
38 % EtOH = 1895 mL EtOH
= 1.39 ppm Ethanol ( Assuming that there is no air ventilation / air exchange in the tunnel )

## Slide 34: Measured vs calculated masses

## Slide 35: Measured vs calculated masses

## Slide 36: Governing Equation
− Concentration of species i measured at the receptor (sample site),
i – The number of chemical species,
j – the number of source types,
− The total mass contribution of source,
−The fraction of species i in emissions from source j.
measured
calculated
  The CMB receptor model consists of a solution to linear equations that express each receptor chemical concentration as a linear sum of products of source profile abundances and source contributions.
Notes: Ci and Fij are measured quantities
Sj is calculated as the result of solving the multiple linear equations. Sj obtained by this method never solve the equations exactly but are the values which come closest to doing so.
Also, model compares if both sides of the equation is equal or not.

## Slide 37: CMB model limitations
CMB analysis focuses on the origins of ambient pollutant (VOC) concentrations rather than the fate of their end products.
Chemically similar sources may result in analytical problems (collinearity).
The method does not directly identify the presence of unknown and unspecified sources, so a considerable proportion of the measured pollutant load may be unexplained;

## Slide 38: CMB model Assumptions:
Composition of the source emissions are constant over the period of ambient and source sampling.
Chemical species do not react with each other (i.e. they add linearly).
All sources with a potential for significantly contributing to the receptor have been identified and have had their emissions characterized.
The source profiles are linearly independent of each other.
Measurement uncertainties are random, uncorrelated and normally distributed.

## Slide 39: VOC patterns (averaged mass concentrations)
Chart: Tunnel. Summer
Chart: Tunnel. Winter
Chart: Inner city. Summer
Chart: Inner city. Winter
Ethanol
Ethanol
Ethanol
Ethanol

## Slide 40
Model results
IDLE
Real Driving
Chart: μg/m3
| Tunnel.S | City center.S
Measured VOCmix | 810.3453 | 91.9868
Gasoline cold start | 364.3081 | 25.0635
Gasoline warm up phase | 2.4409 | 0.64649
Diesel cold start | 44.3558 | 2.0783
Chart: μg/m3
| Tunnel.S | City center.S
Measured VOCmix | 810.3453 | 91.9868
Gasoline cold start | 483.9647 | 33.825
Gasoline warm up phase | 0 | 0
Diesel cold start | 30.322 | 0.06996

## Slide 41: Model Results
After adding artificial source of ethanol
Chart: 
| Tunnel.S | City.S
Measured VOCmix | 810.3453 | 91.9868
Chart: 
| Tunnel.S | City.S
Gasoline cold start | 445.8396 | 35.6262
Gasoline warm up phase | 0 | 0
Diesel cold start | 31.8849 | 0
Ethanol | 201.5405 | 14.1269
Tunnel (S)
City (S)
μg/m3
54 %
84 %

## Slide 42: Data set
Stuttgart
2017 - 2018
Tunnel, Inner city
Sampling in canisters
GC-MS analysis
Source apportionment

## Slide 43: Source apportionment
Chart: VOC source apportionment
| industrial | Traffic | indoor sources | outdor burning | natural sources | home heating
 | 0.3 | 0.35 | 0.08 | 0.1 | 0.12 | 0.05
Source Apportionment (SA) is the practice of deriving information about pollution sources and the amount they contribute to ambient air pollution levels.
Receptor
Notes: Source apportionment (SA) is the technique which relates a source emission (an activity sector or an area) to the ambient air concentration of a pollutant.
This task can be accomplished using three main approaches: Emission inventories, source-oriented models and receptor-oriented models

## Slide 44: introduction
Averaged annual VOC emissions for different source categories replotted from a publication of the German Federal Environmental Agency (UBA).

## Slide 45: European emission standards
Diesel
Gasoline
Notes: Great efforts have been made to reduce vehicle emissions.
The picture shows the development of pollutant limitation within the European Union from the beginning until 2020, Euro 6 for diesel and gasoline engine limitation.

## Slide 46: Voc patterns
Chart: Tunnel (s)
| Ethene | Ethyne | Ethane | Acetaldehyde | Butane | Ethanol | Isopentane | Acetone | Benzene | Toluene | 1,4-diethylbenzene | Other VOCs
 | 34.9748 | 20.3471 | 8.2773 | 14.7879 | 19.0879 | 226.8799 | 29.99 | 67.3815 | 12.7357 | 42.4148 | 2.6453 | 330.8232
 | 15.1789 | 5.7246 | 7.8025 | 6.2509 | 6.4352 | 282.0943 | 7.6644 | 11.7116 | 5.0621 | 7.9327 | 19.5037 | 125.506
 | 2.1621 | 1.2561 | 2.5972 | 6.2455 | 3.1394 | 16.1518 | 4.8216 | 14.9187 | 0.98514 | 3.3517 | 0.2116 | 36.146
 | 4.7552 | 2.919 | 5.9801 | 3.6013 | 5.1518 | 34.5877 | 3.1004 | 4.9095 | 1.6603 | 3.9433 | 6.1938 | 45.6566
Chart: Inner city (S)
| Ethene | Ethyne | Ethane | Acetaldehyde | Butane | Ethanol | Isopentane | Acetone | Benzene | Toluene | 1,4-diethylbenzene | Other VOCs
 | 2.1621 | 1.2561 | 2.5972 | 6.2455 | 3.1394 | 16.1518 | 4.8216 | 14.9187 | 0.98514 | 3.3517 | 0.2116 | 36.146
Summer

## Slide 47: VOC patterns
Winter
Chart: Tunnel (w)
| Ethene | Ethyne | Ethane | Acetaldehyde | Butane | Ethanol | Isopentane | Acetone | Benzene | Toluene | 1,4-diethylbenzene | Other VOCs
 | 15.1789 | 5.7246 | 7.8025 | 6.2509 | 6.4352 | 282.0943 | 7.6644 | 11.7116 | 5.0621 | 7.9327 | 19.5037 | 125.506
Chart: Inner city (w)
| Ethene | Ethyne | Ethane | Acetaldehyde | Butane | Ethanol | Isopentane | Acetone | Benzene | Toluene | 1,4-diethylbenzene | Other VOCs
 | 4.7552 | 2.919 | 5.9801 | 3.6013 | 5.1518 | 34.5877 | 3.1004 | 4.9095 | 1.6603 | 3.9433 | 6.1938 | 45.6566

## Slide 48: VOC patterns
Chart: μg/m3
| Tunnel (S) | Tunnel (W) | Inner city (S) | Inner city (W)
ALKANE | 186.2745 | 57.0681 | 25.0618 | 30.4035
ALKENE | 75.0059 | 24.9422 | 4.4741 | 7.4529
ALKYNE | 20.9591 | 5.7828 | 1.2802 | 2.9336
BIOGENIC | 12.9853 | 4.5822 | 1.3503 | 0.76549
KETONE | 71.8286 | 15.1634 | 16.5156 | 5.8132
ALCOHOL | 237.6891 | 300.1275 | 17.7582 | 35.9066
ALDEHYDE | 15.729 | 8.0986 | 7.8613 | 3.8613
AROMATIC | 155.2053 | 78.9551 | 13.2503 | 32.0372
OTHER | 34.6685 | 6.1469 | 4.4348 | 3.2852
Ethanol is most abundant VOC in urban air.
Ethanol concentrations dominates during both seasons, however in winter they are even higher.
EtOH 95 %
EtOH 91 %
EtOHl 94 %
EtOH 96 %

## Slide 49: VOC patterns
Chart: Tunnel (S)
| ALKANE | ALKENE | ALKYNE | BIOGENIC | KETONE | ALCOHOL | ALDEHYDE | AROMATIC | OTHER
 | 186.2745 | 75.0059 | 20.9591 | 12.9853 | 71.8286 | 237.6891 | 15.729 | 155.2053 | 34.6685
Chart: City Center (S)
| ALKANE | ALKENE | ALKYNE | BIOGENIC | KETONE | ALCOHOL | ALDEHYDE | AROMATIC | OTHER
 | 25.0618 | 4.4741 | 1.2802 | 1.3503 | 16.5156 | 17.7582 | 7.8613 | 13.2503 | 4.4348
Ethanol 95 %
Ethanol 91 %

## Slide 50: VOC patterns
Chart: Tunnel (W)
| ALKANE | ALKENE | ALKYNE | BIOGENIC | KETONE | ALCOHOL | ALDEHYDE | AROMATIC | OTHER
 | 57.0681 | 24.9422 | 5.7828 | 4.5822 | 15.1634 | 300.1275 | 8.0986 | 78.9551 | 6.1469
Chart: City center (W)
| ALKANE | ALKENE | ALKYNE | BIOGENIC | KETONE | ALCOHOL | ALDEHYDE | AROMATIC | OTHER
 | 30.4035 | 7.4529 | 2.9336 | 0.76549 | 5.8132 | 35.9066 | 3.8613 | 32.0372 | 3.2852
Ethanol 94 %
Ethanol 96 %