## Slide 1: Coded lock with digital Elements
Mariam Papava
Agricultural University of Georgia
Student of Electrical and Computer Engineering

## Slide 2: What is a Coded Lock

## Slide 3: why use a Digital lock
No need for a Key
Better Security
User has more control

## Slide 4: My aim with my project
User can change passcode anytime
Order of numbers must matter
Numbers can be repeated in the passcode

## Slide 5: Setting the code
Using DIP (Dual-Inline packet) Switches
In Binary

## Slide 6: Dialing Code
0
1
2
3
Converting decimal to binary with diodes
Maximum number is 9, so we need 4 bits

## Slide 7: Comparing code with dialed number
XNOR |  | 
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
AND |  | 
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 8: Keeping the Order
Counting the number of presses
Assigning outputs to order numbers

## Slide 9: Checking the accuracy of dialed code
RS Latch |  |  | 
S | R | Q | ~Q
0 | 0 | Q | ~Q
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | / | /

## Slide 10: Conclusion
Achieved all my goals
  Order is always checked
  Numbers can be repeated
  Changing the code is very easy
Would add a seven segment display
Have actual lock system using electromagnets

## Slide 11: Thank you for listening