## Slide 1: DETERMINATION OF HEAVY METALS CONTENT IN THE ROOTS OF LICORICE AND VALERIANA BY MICROWAVE PLASMA ATOMIC EMISSION SPECTROMETRY
Bachelor’s student – Natia Tchanturia
Ivane Javakhishvili Tbilisi State University, The Faculty of Exact and Natural Sciences, Department of Chemistry
Supervisors: Prof. Bezhan Chankvetadze & Assistant-Professor - Nino Takaishvili
1
16/09/2022

## Slide 2
HEAVY METALS THAT WE STUDIED
Zn
Pb
Cd
Ni
Cu
Mn
Fe
16/09/2022
2

## Slide 3
Reactive oxygen species (ROS) Production
Damages antioxidants
DNA
Lipids
Proteins
Membrane damage by lipid peroxidation
Protein dysfunction
Loss of DNA repair mechanism
Apoptosis (Programmed cell death)
Alter biological pathways
Heavy metals such as Cd, Pb, Zn,
Cu, Ni, Mn, Fe
Enzyme inhibition
3
16/09/2022

## Slide 4
Valeriana
4
Some Medicinal Plants
Licorice
Licorice Roots
Valeriana
Roots
16/09/2022

## Slide 5
Sample preparation
5
16/09/2022
The roots of Valeriana and Licorice were first ground with a pestle and mortar, then sorted according to quartering, and then sorted further to obtain the particles smaller than 0.1mm. Then they were weighed, dried, and treated with mineral acids. The filtrate was collected, transferred to a volumetric flask, and filled to the mark with DI water.

## Slide 6
Instrumental methods used for heavy metal determination
16/09/2022
6
Atomic Absorbance Spectrometry
Inductively Coupled Plasma Atomic Emission Spectrometry
Microwave Plasma Atomic Emission Spectrometry

## Slide 7
16/09/2022
7
MP-AES - HOW IT WORKS
The magnetron is used to form a plasma from nitrogen gas.
Plasma excites atoms of a specific element.
Atom returns to the ground state and emits light with a wavelength that is characteristic of that element, this light then reaches a detector.
The rate of emission is directly proportional to the number of atoms in the excited state

## Slide 8
Advantages of MP-AES over AAS
Feature | MP-AES | Flame AA
Detection limits | Better | Good
Linear Dynamic Range | Better | Good
Flammable Gas | Not Required | Acetylene
Oxidizing Gas | Not Required | Nitrous oxide
Fuel gas | Not Required | 1-6 tonnes p a
Light sources | Not Required | HC and D2 lamps
Drift correction | Not Required | Double beam
Overnight unattended | Yes | No
Running cost | Lowest | High
Feature | MP-AES | Flame AA
Detection limits | Better | Good
Linear Dynamic Range | Better | Good
Flammable Gas | Not Required | Acetylene
Oxidizing Gas | Not Required | Nitrous oxide
 | Not Required | 1-6 tonnes p a
Light sources | Not Required | HC and D2 lamps
Drift correction | Not Required | Double beam
Overnight unattended | Yes | No
Running cost | Lowest | High
16/09/2022
8
It is More than 2x faster than conventional flame AA
Superior detection limits and improved dynamic range
Cheaper to run and safer since it eliminates the usage of flammable gases
The multi-elemental analysis is possible with MP-AES, but not with AAS

## Slide 9
Experimental
procedure
Preparation of sample
Making standard solutions
Analyzing standards with Microwave Plasma Atomic Emission Spectrometer
Analyzing unknowns with Microwave Plasma Atomic Emission Spectrometer
16/09/2022
9

## Slide 10
MULTISTANDARD
10

## Slide 11: Parameters of the MP-AES
Replicates: 3
Pump Speed (rpm): 20 (Fast pump)
Uptake Time (s): 20
Stabilization Time (s): 20
Number of Pixels: 3
Read Time (s): 3
correlation coefficient limit - 0.9960
Nebulizer Flow:
Cu (324.754 nm) | 0.7 L/min
Zn (213.857 nm) | 0.45 L/min
Ni (352.454 nm) | 0.7 L/min
Cd (228.802 nm) | 0.5 L/min
Pb (405.781 nm) | 0.75 L/min
Mn (403.076 nm) | 0.9 L/min
Fe (371.993 nm) | 0.65 L/min
11
16/09/2022

## Slide 12
Cadmium (Cd)
12
16/09/2022

## Slide 13
Lead (Pb)
13
16/09/2022

## Slide 14
Zinc (Zn)
14
16/09/2022

## Slide 15
Copper (Cu)
15
16/09/2022

## Slide 16
Nickel (Ni)
16
16/09/2022

## Slide 17
Manganese (Mn)
17
16/09/2022

## Slide 18
Iron (Fe)
18
16/09/2022

## Slide 19
The results of the quantitative analysis of Cadmium (Maximum allowed concentration is 0.3 mg/kg According to World Health Organization)
PPM
19
Chart: 
| Cd
Licorice Roots (Kreuter Mix) (02.06.2022) | 0.06
Valeriana Roots (Kreuter Mix) (02.06.2022) | 0.16
Licorice Roots (Bolnisi, Georgia) | 0
Licorice Roots (kazakhstan) | 0
Valeriana Roots (Germany) | 0.23
Valeriana Roots (Georgia) | 0.47
Maximum Allowed Concentration | 0
16/09/2022

## Slide 20
The results of the quantitative analysis of Lead(Maximum allowed concentration is 0.3 mg/kg According to World Health Organization)
PPM
20
Chart: 
| Pb
Licorice Roots (Kreuter Mix) (02.06.2022) | 0.74
Valeriana Roots (Kreuter Mix) (02.06.2022) | 0.06
Licorice Roots (Bolnisi, Georgia) | 1.18
Licorice Roots (kazakhstan) | 1.23
Valeriana Roots (Germany) | 1.63
Valeriana Roots (Georgia) | 4
Maximum Allowed Concentration | 0
16/09/2022

## Slide 21
The results of the quantitative analysis of Zinc (Maximum allowed concentration is 50 mg/kg According to World Health Organization)
PPM
21
Chart: 
| Zn
Licorice Roots (Kreuter Mix) (02.06.2022) | 1.96
Valeriana Roots (Kreuter Mix) (02.06.2022) | 17.42
Licorice Roots (Bolnisi, Georgia) | 14.43
Licorice Roots (kazakhstan) | 13.03
Valeriana Roots (Germany) | 43.25
Valeriana Roots (Georgia) | 39.7
Maximum Allowed Concentration | 0
16/09/2022

## Slide 22
The results of the quantitative analysis of Copper (Maximum allowed concentration is 150 mg/kg According to World Health Organization)
PPM
22
Chart: 
| Cu
Licorice Roots (Kreuter Mix) (02.06.2022) | 23.4
Valeriana Roots (Kreuter Mix) (02.06.2022) | 7.22
Licorice Roots (Bolnisi, Georgia) | 17.88
Licorice Roots (kazakhstan) | 24.7
Valeriana Roots (Germany) | 10.83
Valeriana Roots (Georgia) | 41.07
Maximum Allowed Concentration | 0
16/09/2022

## Slide 23
The results of the quantitative analysis of Nickel (Maximum allowed concentration is 1.5 mg/kg According to World Health Organization)
PPM
23
Chart: 
| Ni
Licorice Roots (Kreuter Mix) (02.06.2022) | 0.76
Valeriana Roots (Kreuter Mix) (02.06.2022) | 3.76
Licorice Roots (Bolnisi, Georgia) | 0.43
Licorice Roots (kazakhstan) | 29.93
Valeriana Roots (Germany) | 10.75
Valeriana Roots (Georgia) | 4.5
Maximum Allowed Concentration | 0
16/09/2022

## Slide 24
The results of the quantitative analysis of Manganese (Maximum allowed concentration is 200 mg/kg According to World Health Organization)
PPM
24
Chart: 
| Mn
Licorice Roots (Kreuter Mix) (02.06.2022) | 13.92
Valeriana Roots (Kreuter Mix) (02.06.2022) | 172.78
Licorice Roots (Bolnisi, Georgia) | 14.33
Licorice Roots (kazakhstan) | 17.2
Valeriana Roots (Germany) | 149.98
Valeriana Roots (Georgia) | 185.6
Maximum Allowed Concentration | 0
16/09/2022

## Slide 25
The results of the quantitative analysis of Iron (Maximum allowed concentration is 200 mg/kg According to World Health Organization)
PPM
25
Chart: 
| Fe
Licorice Roots (Kreuter Mix) (02.06.2022) | 286
Valeriana Roots (Kreuter Mix) (02.06.2022) | 1028
Licorice Roots (Bolnisi, Georgia) | 390.25
Licorice Roots (kazakhstan) | 281.25
Valeriana Roots (Germany) | 688
Valeriana Roots (Georgia) | 2730
Maximum Allowed Concentration | 0
16/09/2022

## Slide 26
№ | Sample | Cd | Pb | Zn | Cu | Ni | Mn | Fe
1 | Licorice Roots (Kräuter Mix), (02.06.2022) | 0.06 | 0.74 | 1.96 | 23.40 | 0.76 | 13.92 | 286.00
2 | Valeriana Roots (Kräuter Mix), (02.06.2022) | 0.16 | 0.06 | 17.42 | 7.22 | 3.76 | 172.78 | 1028.00
3 | Licorice Roots (Bolnisi, Georgia) | - | 1.18 | 14.43 | 17.88 | 0.43 | 14.33 | 390.25
4 | Licorice Roots (Kazakhstan) | - | 1.23 | 13.03 | 24.70 | 29.93 | 17.20 | 281.25
5 | Valeriana Roots (Germany) | 0.23 | 1.63 | 43.25 | 10.83 | 10.75 | 149.98 | 688.00
6 | Valeriana Roots (Georgia) | 0.47 | 4.00 | 39.70 | 41.07 | 4.50 | 185.60 | 2730.00
Content of heavy metals in Valeriana and Licorice roots: (mg/kg)
26
16/09/2022

## Slide 27
Future Plans
Analyze Licorice and Valeriana roots from other
Locations with MP-AES
Use other analytical instruments to cross-check the
results from this study
16/09/2022
27

## Slide 28
Thank You For Your Attention!