## Slide 1
Ivane Javakhishvili Tbilisi State University
Nino Chapidze
Assessment Of Some Heavy Metal Content in the soils of Villages Talaveri, Udabno and The Tissues of Licorice using Microwave Plasma Atomic Emission Spectrometer
Supervisors:
Professor -Bezhan Chankvetadze
Assistant Professor-Nino Takaishvili
Tbilisi 2022
Faculty of Exact and Natural Sciences, Department of Chemistry

## Slide 2: Heavy Metals Toxicity Mechanism
Heavy metals
binding to certain groups of enzymes and proteins(-SH) and inhibition of their activity
Inhibition of neurotransmitter release
replacement of a metallo-enzyme by another metal ion of similar size. For instance, cadmium can replace zinc in certain enzymes, leading to cadmium toxicity. .

## Slide 3: Goal of Analysis
Panorama of the open pit in Bolnisi
“Madneuli”mining plant operates on the basis of copper-lead-zinc ores.
Drawbacks Of Open-Cast Mining
Air Pollution-Heavy Dust Clouds
Destruction of Habitat
Water Consumption
Water Pollution
Soil Contamination with heavy metals

## Slide 4: Instrumentation
Nebulizer
Spray chamber
Peristaltic pump
4210 MP-AES
Pre-Optics window
Waste for larger droplets
Torch
chimney
Plasma viewing port
Nitrogen Plasma

## Slide 5: General Scheme

## Slide 6: Comparison to FAAS
Low Maintanance
MP-AES runs on nitrogen extracted from the air
Improved Safety
Elimination of the usage of flammable gases like acetylene and propane
Improved Analytical Performance
Wider linear range and lower detection limits
Elimination of Chemical Interferences
Lower temperature and reactive atmosphere of flames are most likely to form molecular species. The presence of phosphate in the sample can alter the atomic concentration of calcium due to the formation of relatively nonvolatile complexes. Higher temperature of plasma (5000K) hinders this process
Simplified sample preparation
No need to add releasing agents like Sr or La or exctract metal from interfering material
Agilent 4107 Nitrogen Generator

## Slide 7: Sample Preparation
Soil samples were cleaned of impurities, air dried, grinded and sieved until particles of less than 0.1mm in size were obtained.
Soil samples were further dried at 105-110°C to ensure the removal of moist.
1g of dried sample was placed in aporcelain crucible and dry ashed at 350-400°C in a muffle furnance for 1 hour to combust organic material.
The ash was wet digested with 20 ml aqua regia (3:1 mixture of HCl and HNO3 and) and slowly evaporated to dryness on a hot plate. This procedure was repeated twice. 5 ml of concentrated HCI (diluted twice with deionized water) was added to the final residue, filtered through filter paper with pore size of 0.3μm and made up to 100 ml volume with deionized water.
Plant sample was washed with deionized water. Then its leaves, stem and roots were dissected , air dried and blended to homogenize the sample. 3 g of dried samples were taken and brought up to 50 ml volume employing the same preparation procedures.

## Slide 8: Sample Preparation
№1, 1.1, 1.2, 1.3, 1.4 Sample Solutions

## Slide 9: Common Conditions
Elements | Wavelength(nm) | Detection Limit (μg/L)
Cu | 324.754 | 0.5
Zn | 213.857 | 3.1
Ni | 352.454 | 1.1
Mn | 403.076 | 0.2
Fe | 371.993 | 1.7
Cd | 228.802 | 1.4
Pb | 405.781 | 2.5
Parameter | Setting
Pump Speed (rpm) | 15
Sample Uptake Time(s) | 20
Stabilization Time(s) | 20
Number of Replicates | 3
Background Correction | FLIC
Calibration Fit | Linear

## Slide 10: Sample Information
№ | 1 | 1.1 | 1.2 | 1.3 | 2 | 3 | 4 | 5
Sample | Village Udabno, Kakheti June,2022 | Licorice Roots June, 2022 | Licorice Stem June,2022 | Licorice Leaf June, 2022 | Bolnisi,Village Talaveri,0-30cm, Exp. 1 February 2022 | Bolnisi,Village Talaveri,30-60cm, Exp. 1 February 2022 | Bolnisi,Village Talaveri,0-30cm, Exp.2 February 2022 | Bolnisi,Village Talaveri,30-60cm, Exp. 2 February 2022
Cd (μg/ml) | Ni (μg/ml) | Zn (μg/ml) | Cu (μg/ml) | Mn (μg/ml) | Fe (μg/ml) | Pb (μg/ml)
0 | 0 | 0 | 0 | 0 | 0 | 0
0.005 | 0.005 | 0.05 | 0.2 | 0.5 | 1 | 0.01
0.01 | 0.01 | 0.1 | 0.4 | 1.0 | 2 | 0.05
0.05 | 0.05 | 0.5 | 0.8 | 2.0 | 3 | 0.1
0.1 | 0.1 | 1 | 1 | 5.0 | 5 | 1
1 | 1 | 2 | 2 | 6.0 |  | 2
Standard Solution Concentrations for External Clibration

## Slide 11
Results and Data Analysis
Calibration Curves of Elements for Samples № 1 , 1.1, 1.2, 1.3
Zinc
Cadmium

## Slide 12
Results and Data Analysis
Calibration Curves of E lements for Samples № 1 , 1.1, 1.2, 1.3
Copper
Nickel

## Slide 13
Results and Data Analysis
Calibration Curves of Elements for Samples № 1 , 1.1, 1.2, 1.3
Lead
Iron

## Slide 14
Results and Data Analysis
Calibration Curves of Elements for Samples № 1 , 1.1, 1.2, 1.3
Manganese

## Slide 15: Results and Data Analysis
Content mg/kg |  |  |  |  |  |  |  | 
№ | Sample | Cd | Pb | Zn | Cu | Ni | Mn | Fe
1 | Udabno soil | 0.8 | 4.7 | 63.7 | 40.4 | - | 1056 | 36900
1.1 | Licorice Root | 0.05 | 7.9 | 15.25 | 19.1 | 3.65 | 14.8 | 155.5
1.2 | Licorice Stem | - | 8.0 | 6.22 | 10.4 | 0.96 | 14.1 | 48.1
1.3 | Licorice Leaf | - | 2.9 | 9.33 | 7.4 | 0.7 | 65.7 | 153.1
MPL in Soils |  | 0.5-2 | 20-30 | 100 | 55 | 85 | 1500 | 
MPL in Medicinal Plants (WHO) |  | 0.3 | 10 | 50 | 20-150 | 1.5 | 200 | 200
MPL-Maximum Permissible Limit

## Slide 16: Results and Data Analysis
Chart: Zinc Distribution
| Zinc
Root | 15.25
Stem | 6.22
Leaf | 9.33
Chart: Copper Distribution
| Copper
Root | 19.1
Stem | 10.4
Leaf | 7.4
Zinc (Zn)
Copper (Cu)
Root>Leaf>Stem
Root>Stem>Leaf

## Slide 17: Results and Data Analysis
LEAD (Pb)
Chart: Lead Distribution
| Lead
Root | 7.9
Stem | 8
Leaf | 2
Stem>Root>Leaf
Chart: Nickel Distribution
| Nickel
Root | 3.65
Stem | 0.96
Leaf | 0.7
Nickel (Ni)
Root>Stem>Leaf

## Slide 18
Chart: Iron Distribution
| Iron
Root | 155.5
Stem | 48.1
Leaf | 153.1
Results and Data Analysis
Chart: Manganese Distribution
| Manganese
Root | 14.8
Stem | 14.1
Leaf | 65.7
Manganese (Mn)
Iron (Fe)
Root>Leaf>Stem
Leaf>Root>Stem

## Slide 19: Results and Data Analysis
Calibration Curves of Elements for Samples № 7 , 8, 9, 10
Nickel
Lead

## Slide 20: Results and Data Analysis
Calibration Curves of Elements for Samples № 7 , 8, 9, 10
Zinc
Copper

## Slide 21: Results and Data Analysis
Calibration Curves of Elements for Samples № 7 , 8, 9, 10
Manganese
Iron

## Slide 22: Results and Data Analysis
Calibration Curves of Elements for Samples № 7 , 8, 9, 10
Cadmium

## Slide 23: Results and Data Analysis
Content mg/kg |  |  |  |  |  |  |  | 
№ | Sample | Cd | Pb | Zn | Cu | Ni | Mn | Fe
2 | Bolnisi, Village Talaveri, 0-30cm, Exp.1 | 1.8 | 6.0 | 112.0 | 84.0 | 63.0 | 900.0 | 38.30
3 | Bolnisi Village Talaveri, 30-60cm, Exp.1 | 0.98 | 4.0 | 72.0 | 41.0 | 54.0 | 770.0 | 34.90
4 | Bolnisi, Village Talaveri,0-30cm, Exp.2 | 0.6 | 3.0 | 86.0 | 59.0 | 61.0 | 900.0 | 37.00
5 | Bolnisi, Village Talaveri, 30-60cm, Exp.2 | 0.4 | 2.0 | 72.0 | 48.0 | 52.0 | 790.0 | 34.40
MPL in Soils |  | 0.5-2 | 20-30 | 100 | 55 | 85 | 1500 | 
g/kg

## Slide 24: Summary
Industrialization and human activities have increased our exposure to heavy metals and harmful substances,which inspired our analysis. From the obtained results, we can conclude that territories in close proximity to mining sites can be affected at some extent , thus further research is necessary to provide us with more detailed explanation of mechanisms of heavy metal distribution and accumulation in the biome.

## Slide 25: References
G. Supatashvili, Environmental Chemistry, Tsu, 2009
Baba, H. S. and Mohammed, M. I. Determination of Some Essential Metals in Selected Medicinal Plantshttps://www.ajol.info/index.php/csj/article/view/209959/197947
WHO- guidelines for assessing quality of herbal medicines with reference to contaminants and residuehttps://apps.who.int/iris/handle/10665/43510
Donald M. West, Douglas A. Skoog, F.James Holler, Stanley R. Crouch- Fundamentals Of Analytical Chemistry, 9th edition

## Slide 26: Thanks For Attention!
¯\_(ツ)_/¯