## Slide 1: Diurnal and annual cycle of Nitrogen Oxides
ROBERT WEGENER

## Slide 2: Diurnal and annual cycle of Nitrogen Oxides
SmartLab Opening 27/09/2017

## Slide 3: Diurnal and annual cycle of Nitrogen Oxides
SmartLab Opening 27/09/2017
11 Month of continuous data of CO2, CO, CH4, NO, NO2 and ozone

## Slide 4: Diurnal and annual cycle of Nitrogen Oxides
Diurnal cycles of ozone / CO2 in June

## Slide 5: Diurnal and annual cycle of Nitrogen Oxides
From: Stull, 1988
part of the
atmosphere that is strongly influenced directly by the presence of the surface
of the earth
Day time boundary layer is usually very turbulent, due to ground-level heating
Thickness varies between 100 and 3000m in time
Strong diurnal variations
The Planetary Boundary Layer (PBL)

## Slide 6: Diurnal and annual cycle of Nitrogen Oxides
Diurnal evolvement of the boundary layer in high pressure regions
From: Stull, 1988
Virtual potential temperature
Virtual temperature is the temperature that dry air must
have to equal the density of moist air at the same pressure
Mixed Layer
Notes: sun heats the surface during daytime
surface is cooling during the night due to thermal radiation
5-10°C temperature difference day/night at the surface
air temperature above the surface follows slowly
temperature above 400m shows almost no variation
surface temperature is the driver for vertical mixing even with moderate wind
At and shortly after sunrise, surface heating causes turbulent eddies to develop,
producing a mixed layer whose depth grows to a maximum depth in late morning.
In this mixed layer, potential temperature and water vapor mixing ratio are nearly
uniform.

## Slide 7: Diurnal and annual cycle of Nitrogen Oxides
Diurnal evolvement of the boundary layer in high pressure regions
From: Stull, 1988
Stable Boundary Layer formed
Notes: At the sunset, the deep surface cooling creates a stable (nocturnal) boundary
layer, above which is a residual layer, basically the leftover part of the daytime
mixed layer

## Slide 8: Diurnal and annual cycle of Nitrogen Oxides
Diurnal evolvement of the boundary layer in high pressure regions
From: Stull, 1988
Residual Layer (detached from ground)

## Slide 9: Diurnal and annual cycle of Nitrogen Oxides
Diurnal evolvement of the boundary layer in high pressure regions
From: Stull, 1988
Mixed Layer fomed again

## Slide 10: Diurnal and annual cycle of Nitrogen Oxides
Diurnal evolvement of the boundary layer in high pressure regions
From: Stull, 1988
Mixed Layer
developped

## Slide 11: Diurnal and annual cycle of Nitrogen Oxides
Residual
Layer RL
Residual
Layer RL
Planetary
Boundary
Layer PBL
Nocturnal Boundary
Layer NBL
NBL
Diurnal evolvement of the boundary layer in high pressure regions
m
2000
800
400
50
sunrise
sunset
00:00 6:00 12:00 18:00 24:00

## Slide 12: Diurnal and annual cycle of Nitrogen Oxides
Concentration of pollutants emitted from the ground (local sources, e.g. NOx,CO2)
m
2000
800
400
50
sunrise
sunset
00:00 6:00 12:00 18:00 24:00

## Slide 13: Diurnal and annual cycle of Nitrogen Oxides
Concentration of pollutants emitted from the ground (local sources, e.g. NOx)
lifting of the mixing layer
Mixing layer is fully developed
Nocturnal boundary
layer is developing
Nox, CO, CO2, CH4
concentrations are
highest in the early
morning

## Slide 14: Diurnal and annual cycle of Nitrogen Oxides
Concentration of pollutants emitted from the ground (local sources)
sunrise
sunset
Notes: Sunrise 5:30
Sunset 20:30

## Slide 15: Diurnal and annual cycle of Nitrogen Oxides
Concentration of pollutants emitted from the ground (local sources, e.g. NOx)
Position of the SmartLab

## Slide 16: Diurnal and annual cycle of Nitrogen Oxides
Concentration of pollutants emitted from the ground (local sources)
sunrise
sunset
Notes: Sunrise 5:30
Sunset 20:30

## Slide 17: Diurnal and annual cycle of Nitrogen Oxides
Concentration of pollutants with no local sources, e.g. Ozone
m
2000
800
400
50
sunrise
sunset
00:00 6:00 12:00 18:00 24:00

## Slide 18: Diurnal and annual cycle of Nitrogen Oxides
Concentration of pollutants with no local sources, e.g. Ozone
m
2000
800
400
50
sunrise
sunset
00:00 6:00 12:00 18:00 24:00
Can it be measured ?

## Slide 19: Diurnal and annual cycle of Nitrogen Oxides
Concentration of pollutants with no local sources, e.g. Ozone
m
2000
800
400
50
sunrise
sunset
00:00 6:00 12:00 18:00 24:00

## Slide 20: Diurnal and annual cycle of Nitrogen Oxides
Concentration of pollutants with no local sources, e.g. Ozone
lifting of the mixing layer
Mixing layer is fully developed
Nocturnal boundary
layer is developing
Ozone
Concentrations is
highest during the day

## Slide 21: Diurnal and annual cycle of Nitrogen Oxides
Concentration of pollutants with no local sources, e.g. Ozone
photochemical
production
of ozone
lifting of the mixing layer
Mixing layer is fully developed
Nocturnal boundary
layer is developing

## Slide 22: Diurnal and annual cycle of Nitrogen Oxides
Median Ozone data June 2018
sunrise
sunset

## Slide 23: Diurnal and annual cycle of Nitrogen Oxides
The ratio of NO to NO2 is governed by the photostationary state (PSS)
NO2 + hn NO + O ; J(NO2)
O + O2 + M  O3 + M ; very fast
NO + O3  NO2 + O2 ; k(NO+O3)

## Slide 24: Diurnal and annual cycle of Nitrogen Oxides
The ratio of NO to NO2 is governed by the photostationary state (PSS)
NO2 + hn NO + O ; J(NO2)
O + O2 + M  O3 + M ; very fast
NO + O3  NO2 + O2 ; k(NO+O3)

## Slide 25: Diurnal and annual cycle of Nitrogen Oxides
The ratio of NO to NO2 is governed by the photostationary state (PSS)
NO2 + hn NO + O ; J(NO2)
O + O2 + M  O3 + M ; very fast
NO + O3  NO2 + O2 ; k(NO+O3)

## Slide 26: Diurnal and annual cycle of Nitrogen Oxides
The ratio of NO to NO2 is governed by the photostationary state (PSS)
NO2 + hn NO + O ; J(NO2)
O + O2 + M  O3 + M ; very fast
NO + O3  NO2 + O2 ; k(NO+O3)

## Slide 27: Diurnal and annual cycle of Nitrogen Oxides
The ratio of NO to NO2 is governed by the photostationary state (PSS)
NO2 + hn NO + O ; J(NO2)
O + O2 + M  O3 + M ; very fast
NO + O3  NO2 + O2 ; k(NO+O3)

## Slide 28: Diurnal and annual cycle of Nitrogen Oxides
The ratio of NO to NO2 is governed by the photostationary state (PSS)
NO2 + hn NO + O ; J(NO2)
O + O2 + M  O3 + M ; very fast
NO + O3  NO2 + O2 ; k(NO+O3)
caused by the early onset of JNO2 and the shifted lifting of the mixing layer
Zero at night

## Slide 29: Diurnal and annual cycle of Nitrogen Oxides
The ratio of NO to NO2 is governed by the photostationary state (PSS)
Hourly medians for June
sunrise
sunset

## Slide 30: Diurnal and annual cycle of Nitrogen Oxides
Annual cycles of compounds with local sources

## Slide 31: Diurnal and annual cycle of Nitrogen Oxides
Annual cycle of nitrogen oxides

## Slide 32: Diurnal and annual cycle of Nitrogen Oxides
Annual cycle of nitrogen oxides
Zero at night

## Slide 33: Diurnal and annual cycle of Nitrogen Oxides
Annual cycle of nitrogen oxides

## Slide 34: Diurnal and annual cycle of Nitrogen Oxides
Annual cycle of nitrogen oxides
Larger than zero at night
Second peak due to traffic

## Slide 35: Diurnal and annual cycle of Nitrogen Oxides
Annual cycle of nitrogen oxides

## Slide 36: Diurnal and annual cycle of Nitrogen Oxides
Summary
High NO2 and NO values in winter
High ozone values in summer
Data affected from highly-trafficked
Street nearby.
How is the situation at other sites ?
See talks on Friday morning

## Slide 37: Diurnal and annual cycle of Nitrogen Oxides
Summary
High NO2 and NO values in winter
High ozone values in summer
Data affected from highly-trafficked
Street nearby.
How is the situation at other sites ?
See talks on Friday morning
Thank you,
გმადლობთ

## Slide 38: Diurnal and annual cycle of Nitrogen Oxides
Summary
High NO2 and NO values in winter
High ozone values in summer
Data affected from highly-trafficked
Street nearby.
How is the situation at other sites ?
See talks on Friday morning

## Slide 39: Diurnal and annual cycle of Nitrogen Oxides
Annual cycle of nitrogen oxides
NO2 + hn NO + O ; J(NO2)
O + O2 + M  O3 + M ; very fast
NO + O3  NO2 + O2 ; k(NO+O3)

## Slide 40: Diurnal and annual cycle of Nitrogen Oxides
Annual cycle of nitrogen oxides
NO2 + hn NO + O ; J(NO2)
O + O2 + M  O3 + M ; very fast
NO + O3  NO2 + O2 ; k(NO+O3)

## Slide 41: Diurnal and annual cycle of Nitrogen Oxides

## Slide 42: Diurnal and annual cycle of Nitrogen Oxides
Concentration of pollutants with no local sources, e.g. Ozone
sunrise
sunset
00:00 6:00 12:00 18:00 24:00
surface observation
NBL
RL at 800m
ppb
60
40
20
0
Ozone

## Slide 43: Diurnal and annual cycle of Nitrogen Oxides
Summary
High NO2 and NO values in winter
High ozone values in Summer
Data affected from highly trafficked
Street nearby
How is the situation at other sites ?
See talks on Friday morning

## Slide 44: Diurnal and annual cycle of Nitrogen Oxides
Summary
High NO2 and NO values in winter
High ozone values in Summer
Data affected from highly trafficked
Street nearby
How is the situation at other sites ?
See talks on Friday morning

## Slide 45: Diurnal and annual cycle of Nitrogen Oxides
Summary
High NO2 and NO values in winter
High ozone values in Summer
Data affected from highly trafficked
Street nearby
How is the situation at other sites ?
See talks on Friday morning

## Slide 46: Diurnal and annual cycle of Nitrogen Oxides
Nitrogen oxides at highly trafficked streets
Weekend effect.
NO > zero, also at night.
Source: Join database
https://join.fz-juelich.de

## Slide 47: Diurnal and annual cycle of Nitrogen Oxides
Annual cycle of nitrogen oxides
NO2 + hn NO + O ; J(NO2)
O + O2 + M  O3 + M ; very fast
NO + O3  NO2 + O2 ; k(NO+O3)

## Slide 48: Diurnal and annual cycle of Nitrogen Oxides
Annual cycle of CO, CH4, CO2
sunrise
sunset

## Slide 49: Diurnal and annual cycle of Nitrogen Oxides
Annual cycle of nitrogen oxides
NO2 + hn NO + O ; J(NO2)
O + O2 + M  O3 + M ; very fast
NO + O3  NO2 + O2 ; k(NO+O3)

## Slide 50: Diurnal and annual cycle of Nitrogen Oxides
Annual cycle of nitrogen oxides
NO2 + hn NO + O ; J(NO2)
O + O2 + M  O3 + M ; very fast
NO + O3  NO2 + O2 ; k(NO+O3)

## Slide 51: Diurnal and annual cycle of Nitrogen Oxides
Diurnal evolvement of the boundary layer in high pressure regions
m
2000
800
400
50
sunrise
sunset
00:00 6:00 12:00 18:00 24:00

## Slide 52: Diurnal and annual cycle of Nitrogen Oxides
The ratio of NO to NO2 is governed by the photostationary state (PSS)
NO2 + hn NO + O ; J(NO2)
O + O2 + M  O3 + M ; very fast
NO + O3  NO2 + O2 ; k(NO+O3)
caused by the early onset of JNO2 and the shifted lifting of the mixing layer

## Slide 53: Diurnal and annual cycle of Nitrogen Oxides
Nitrogen oxides at highly trafficked streets

## Slide 54: Diurnal and annual cycle of Nitrogen Oxides
Temporal evalution of the planetary boundary Layer

## Slide 55: Messungen TP6 für die DRITTE IOP-STUTTGART (07.02.18 – 23.02.18)
Mobile Messungen Messrouten:
Krummbachtal
Neckartor
Feuerbach
Heslacher Tunnel

## Slide 56: Messungen TP6 für die DRITTE IOP-STUTTGART (07.02.18 – 23.02.18)
Route um das Neckartor
Mobile Messungen Messrouten Neckartor
Neckartor

## Slide 57: Messungen TP6 für die DRITTE IOP-STUTTGART (07.02.18 – 23.02.18)
Übersicht Messfahrten
Mobile Messungen MOBILAB:
Datum | Name
23.02.2018 | Stuttgart -> FZJ
22.02.2018 | Neckartorrunde / Heslachtunnel (3x), Kaltenbachtal, Krummbachtal, Sonnenberg
21.02.2018 | Neckartorrunde / Heslachtunnel (3x), Kaltenbachtal, Krummbachtal, Sonnenberg
20.02.2018 | FZJ -> Stuttgart
15.02.2018 | Rückfahrt Stuttgart FZJ
14.02.2018 | Neckartorrunde / Heslachtunnel (4x), Kaltenbachtal
13.02.2018 | Neckartorrunde / Heslachtunnel (4x), Kaltenbachtal
12.02.2018 | Uni Vaihingen Feuerbachrunde
11.02.2018 | Uni Vaihingen, Feuerbachrunde, Krummbachtal
10.02.2018 | Neckartorrunde / Heslachtunnel (3x) , Uni Vaihingen
09.02.2018 | Neckartorrunde / Heslachtunnel (4x) , Krummbachtal
08.02.2018 | Neckartorrunde / Heslachtunnel (5x)
07.02.2018 | Hinfahrt

## Slide 58: Messungen TP6 für die DRITTE IOP-STUTTGART (07.02.18 – 23.02.18)
NO2 [ppb]
NO2 um das Neckartor (13.02.2018)
06:00
09:00
12:00
15:00
18:00
Ausgeprägter NO2
Tagesgang.
Starke Unterschiede
westlich und östlich
der B14.

## Slide 59: Messungen TP6 für die DRITTE IOP-STUTTGART (07.02.18 – 23.02.18)
N2O [ppb]
NO2 / N2O um das Neckartor (13.02.2018)
09:00
12:00
15:00
18:00
NO2 [ppb]
N2O ist wie NO2 entlang der B14 erhöht, zeigt z.T. aber andere Features

## Slide 60: Messungen TP6 für die DRITTE IOP-STUTTGART (07.02.18 – 23.02.18)
NO2 / N2O um das Neckartor (13.02.2018)
From: HAUSBERGER, Stefan: N2O aus mobilen Quellen. In: ACCC-Workshop „N2O und das Kyoto-Ziel“,
Universität für Bodenkultur, Wien. 1999, S. 1–14. URL: http://www.accc.gv.at/pdf/no-hausberger.pdf
Das Verhältnis von
N2O zu NOx-Emissionen
unterschiedet sich.

## Slide 61: VieRTE IOP StuTTGART
Messungen im Luv / Lee der Stadt
Messungen im Luv / Lee der Stadt
Mobile Messungen zusammen mit DLR:
WIND
WIND