## Slide 1
8TH GEORGIAN – GERMAN SCHOOL AND WORKSHOP IN BASIC SCIENCE
Current projects at AtmoSim_lab
Supervisors:
Full Professor Bezhan Chankvetadze
Assistant-professor Giorgi Jibuti
PhD student: Ketevan Kharaishvili
August 20–25
Tbilisi,2018
Ivane Javakhishvili Tbilisi State University
School of Exact and Natural Sciences

## Slide 3
Gas Phase Composition of the Atmosphere
 | Basic components | Trace gases
Permanent gases | Nitrogen( N2); Oxygen (O2); Argon (Ar) | Other Noble gases
Volatile gases | Carbon dioxide (CO2) | Other long lifetime gases
Highly volatile gases | Water vapor | Other short lifetime gases
Amount
Atmospheric Lifetime
Classification of atmospheric gases

## Slide 4
Pollution sources:
Transportation
Energy Production
Biomass Burning
Forest Fire
Volcanoes Eruption

## Slide 5
Measurements at SMART|AtmoSim_LAB
The laboratory equipment that we used;
Some of the gas measurement and monitoring in Tbilisi;
The methods of atmospheric measurement which we used in laboratory;

## Slide 6
Picarro CRDS CO2;CO; CH4; H2O;
NOx
(NO + NO2)
Ozone monitor

## Slide 7
Definition:
NOx=NO(nitrogen monoxide)+NO2(nitrogen dioxide)
NOx has different chemistry at day time and at night time
-Day: photolysis and thermal reactions
-Night: thermal reactions only

## Slide 8
Nitrogen compounds (NO,NO2) via chemiluminescence with O3
The 𝑵𝑶 + 𝑶3 reaction
𝑵𝑶 + 𝑶3 → 𝑵𝑶2 + 𝑶2
𝑵𝑶 + 𝑶3 → 𝑵𝑶2*+ 𝑶2
𝑵𝑶2* → 𝑵𝑶2 + 𝒉𝝂
𝑵𝑶2*+ 𝑴 → 𝑵𝑶2 + 𝑴
NO2 is converted to NO
𝒉𝝂
𝟐𝑵𝑶𝟐→𝟐𝑵𝑶+𝑶𝟐
NO+ O3 → 𝑵𝑶2 + 𝑶2

## Slide 9
NOx analyzer
Blue Light Converter efficiency 30 %

## Slide 10
CLD 780TR, Unit-CPS (Count Per Second)
Measure of NOx
NOx equipment works in the following mode:
Z- Zero mode, without O3 Generator
M-Measure mode, with O3 Generator
NO-measure
NO Calculation
[NO]= (M-Z(cps)) × Sensitivity (PPB/CPS)

## Slide 11
NO2 with NO2 Converter
l- Zero mode, without O3 Generator
L- with O3 Generator
NO2 = NO - NO
Conv
NO2 -measure
NO2 Calculation
[𝑳 − 𝒍 − (𝑴 − 𝒁 )
𝑵𝑶]𝟐 =
Sensitivity × Efficiency

## Slide 13
Picarro CRDS CO2;CO; CH4; H2O;
NOx
(NO + NO2)
Ozone monitor

## Slide 14
Cavity Ringdown Spectrometer

## Slide 17
Determination of ozone with ultraviolet photometry
Ozone is measured by absorbance of corresponding wavelength of UV light by air sample inside gas cuvete

## Slide 18
Measurements with cylinders
Preparing cylinders for sampling
Sampling
Analysis

## Slide 19
Cylinders washing and Drain system

## Slide 20
Sampling
Tsereteli
Atmospheric measurements in Tbilisi
Marjanishvili
Rustaveli
Last three months:

## Slide 21
Write data and process results
Analysis
By washing and drain system prior to analysis we dilute the samples up to 3 atmospheric pressure with the use of Argon and start analysis.
As we have already mentioned that picarro gives us ready results which we use directly

## Slide 22
Contamination gradients for air pollutants in time
Rush hour in the morning
Not during rush hour in the afternoon
Rush hour in the evening

## Slide 23
Contamination gradients for air pollutants in space
To exclude the inaccuracy we perform sampling in a room and compare it to online
We were distributed with 10 cylinders ( 2 of them stay in room) on a TSU nearby location and sampling with online.

## Slide 24
Thank you for your attention!