## Slide 1: Nitrogen Oxides Pollution in Tbilisi
Master Student – Tamar Khatiashvili
Ivane Javakhishvili Tbilisi State University, The Faculty of Exact and Natural Sciences, Department of Chemistry
Supervisors: Full Professor, Full Member of the Georgian National Academy of Sciences – Bezhan Chankvetadze & Assistant-professor – Giorgi Jibuti

## Slide 2: Composition of Air
Nitrogen -78.084%
Oxygen -20.946%
Carbon dioxide -0.039%
Argon -0.934%
All others-0.1%
Water vapor -1%

## Slide 3
Urban
fires
8/24/2018

## Slide 4
Air Pollution in Georgia by Sources
2000-2013 Years
Ministry of Environment and Natural Resources Protection of Georgia
Transport
Industry
Energy
8/24/2018

## Slide 5
NOx Emissions in Georgia, 2000-2009 Years
Ministry of Environment and Natural Resources Protection of Georgia
Industrial Sources
Energy
Transportation
Thousand tons
Year
8/24/2018

## Slide 6: What Are the Environmental Impacts of NOx?
NOx
Mobile – NOx can be transported long distances on prevailing winds
Ground level Ozone (SMOG) – from NOx + VOC’s damage to lungs, vegetation & crops
Acid Rain – damages forests, buildings & water sources
Visibility – Nitrates & NO2 block light, reduces visibility
Global Warming - Greenhouse gases in the atmosphere trap heat, keeping the earth warm. N2O is much more damaging than CO2
Particles – NOx reacts to formic acid vapor & particles, Penetrate lungs – emphysema, bronchitis, respiratory disease
8/24/2018

## Slide 7: Automatic Station
Varketili
Vashlijvari
Kazbegi Avenue
Tsereteli Avenue
NO2, mg/m3
Ministry of Environment and Natural Resources Protection of Georgia
8/24/2018

## Slide 8: Research Methods Overview of Nitrogen Oxides
Infrared spectroscopy
Ultraviolet-visible spectroscopy
Laser induced fluorescence
Chemiluminescence
8/24/2018

## Slide 9: Laboratory Equipment
8/24/2018

## Slide 10: Chemical Cycle of NOx
𝑵𝑶x = 𝑵𝑶 + 𝑵𝑶2
Nitrogen oxides (NO and NO2, referred together as NOx) are highly reactive gases formed when oxygen and nitrogen react at high temperatures during combustion. At this time this reaction takes place:
𝑵2+𝑶2→2𝑵𝑶
After a few hours NO is converted to NO2. NO2 reacts further with other substances in the air to form nitric acid, particulate matter and substances called PANs (peroxyacyl nitrates).
𝑵𝑶+𝑶3→𝑵𝑶2+𝑶2
NO2 is harmful for health.
Also with sunlight NO2 can convert back to NO and produce ozone (O3) as a side pollutant. Because of the potential of NO2 to produce these "secondary" pollutants, it is important to monitor and regulate NO2.
8/24/2018

## Slide 11
NO and NO2 are measured by the chemiluminescence method. Chemiluminescence is the emission of light, as the result of a chemical reaction.
𝑵𝑶+𝑶3→𝑵𝑶2+𝑶2
𝑵𝑶+𝑶3→𝑵𝑶2*+𝑶2
𝑵𝑶2*→𝑵𝑶2+𝒉𝝂 (chemiluminescence)
𝑵𝑶2*+𝑴→𝑵𝑶2+𝑴
𝑵𝑶2 is converted to 𝑵𝑶
𝟐𝑵𝑶𝟐 + 𝒉𝝂→𝟐𝑵𝑶+𝑶𝟐
8/24/2018

## Slide 12: Scheme of the NOX Analyzer
8/24/2018
Notes: Photomultiplier tube NO2--NO

## Slide 13
Maximum allowed concentrations (considering 1 atm pressure and 200C temperature):
Gas
Limit (ppb)
Limit (µg/m³)
8/24/2018

## Slide 14: SMART|AtmoSim_LAB
8/24/2018

## Slide 15
8/24/2018
Contamination Gradients for NOx in Time

## Slide 16: Vake Park in Rush Hour
8/24/2018
Chart: (31.03.2018)
| Morning | Afternoon | Evening | Limit
NO | 0.35 | 0 | 5.91 | 40.9
NO2 | 19.5 | 13.4 | 3.1 | 21.3

## Slide 17: Mushthaid Garden in Rush Hour
8/24/2018
Chart: (30.03.2018)
| Morning | Afternoon | Evening | Limit
NO | 1.02 | 0.16 | 0.98 | 40.9
NO2 | 16.3 | 23.02 | 10.05 | 21.3

## Slide 18: Varaziskhevi Street in Rush Hour
Chart: (28.03.2018)
| Morning | Afternoon | Evening | Limit
NO | 399.03 | 478.21 | 183.23 | 40.9
NO2 | 113.65 | 108.03 | 101.22 | 21.3
8/24/2018

## Slide 19: Marjanishvili Square in Rush Hour
Chart: (28.03.2018)
| Morning | Afternoon | Evening | Limit
NO | 92 | 1.94 | 31.8 | 40.9
NO2 | 47.45 | 32.61 | 92.47 | 21.3
8/24/2018

## Slide 20: Didi Dighomi & Saakadze Square in Rush Hour
Chart: Didi Dighomi (29.03.2018)
| Morning | Afternoon | Evening | Limit
NO | 77.1 | 85.5 | 119.9 | 40.9
NO2 | 4.5 | 4 | 4.8 | 21.3
Chart: Saakadze Square (24.03.2018)
| Morning | Afternoon | Evening | Limit
NO | 37.1 | 74.2 | 81.8 | 40.9
NO2 | 4.5 | 29.2 | 5.5 | 21.3
8/24/2018

## Slide 21: Station Square in Rush Hour
Chart: (27.03.2018)
| Morning | Afternoon | Evening | Limit
NO | 20.7 | 3.2 | 60.1 | 40.9
NO2 | 19.1 | 34.9 | 85.8 | 21.3
8/24/2018

## Slide 22: Freedom Square in Rush Hour
Chart: (27.03.2018)
| Morning | Afternoon | Evening | Limit
NO | 236.39 | 46.86 | 3.91 | 40.9
NO2 | 40.29 | 75.99 | 3 | 21.3
8/24/2018

## Slide 23
8/24/2018
Contamination Gradients for NOx in Space

## Slide 24: Near the University Area
Chart: Avarage Concentration of NO
| NO
Chavchavadze Avenue N2 | 8.3033
Melikishvili Avenue N14 | 85.7567
School N51 | 61.9167
Varaziskhevi Street | 77.1
Tbilisi Concert Hall | 53.8667
Chachava Clinic | 85.3333
Limit | 40.9
Chart: Avarage Concentration of NO2
| NO2
Chavchavadze Avenue N2 | 47.8
Melikishvili Avenue N14 | 35.8
School N51 | 62.2367
Varaziskhevi Street | 68.9
Tbilisi Concert Hall | 70.8333
Chachava Clinic | 92.45
Limit | 21.3
8/24/2018

## Slide 25: Around the University
Chart: Concentration (ppb)
| Chavchavadze | Yard of first building | Varaziskhevi street | Entrance gate of second building | Limit
NO | 240.7 | 0.02 | 401.9 | 0.07 | 40.9
NO2 | 103.6 | 48.4 | 100.7 | 35.9 | 21.3
(22.03.2018)
8/24/2018
Avenue N1

## Slide 26: Varaziskhevi Street
Chart: NO
| NO
Varaziskhevi Street | 513.2 | 254.5 | 120.5 | 349.6 | 82.6
Limit | 40.9 | 40.9 | 40.9 | 40.9 | 40.9
Chart: NO2
| NO2
Varaziskhevi Street | 62.9 | 56.3 | 33.3 | 51.6 | 27.7
Limit | 21.3 | 21.3 | 21.3 | 21.3 | 21.3
8/24/2018
(23.03.2018)

## Slide 27: Tsereteli Avenue
Chart: Avarage Concentration of NO
| NO
Metro Didube | 30.279
Dinamo | 121.079
Exhibition | 147.07
Limit | 40.9
Chart: Avarage Concentration of NO2
| NO2
Metro Didube | 63.96
Dinamo | 77.318
Exhibition | 78.22
Limit | 21.3
8/24/2018

## Slide 28: Marjanishvili Area
Chart: Avarage Concentration of NO
| NO
McDonald's | 5.9479
Zaarbriuken Square | 32.1257
Danish House | 48.7171
Limit | 40.9
Chart: Avarage Concentration of NO2
| NO2
McDonald's | 57.4286
Zaarbriuken Square | 67.98
Danish House | 42.0871
Limit | 21.3
8/24/2018

## Slide 29: Conclusions
The most polluted areas in Tbilisi:
N3 Marjanishvili square
N2 Tsereteli avenue
N1 Varaziskhevi street
Sampling needs about 30 seconds. NO and NO2 concentrations are very variable, that’s why a number of measurements are required for the average results.
We do online measurements of NO and NO2 for more representative data.
In areas where road vehicles are the main source of NOx there is often higher NO2 concentrations during peak traffic times such as around 7pm weekdays.
The ozone (O3) concentration increases during the day while the NO2 concentration decreases. That's because NO2 transforms to NO in the presence of sunlight.
After 6 PM, the NO2 concentration builds up as there is no sunlight to convert NO2 back to NO.
Traffic is the main reason
The cleanest areas in Tbilisi: Vake Park & Mushthaid Garden
8/24/2018

## Slide 30
NO2 Emissions in Stuttgart
NO2 ppb
Neckartor
Tunnel
University
Results of mobile NO2 measurements in the area of the city of Stuttgart. Lowest winter values are found with less than 21 ppb NO2 upstream of the city (Vaihingen, Kalltal, Krummbachtal), while in the area of the E-14 in the city center the observed local background values consistently exceed 99 ppb.
8/24/2018

## Slide 31
Acknowledgements:
Tbilisi City Hall
8/24/2018

## Slide 32
Thank you for your attention!
Before
After
8/24/2018