## Slide 1: Climate research at FZJ and perspectives at TSU Is urban air pollution now coming from the broom closet?
nana khundadze

## Slide 2
VOCs: impact on air quality
Short-lived
greenhouse
gases
Oxidation
chemistry
O3, particles
CO, CH4, NOx, SO2, VOC
+OH
Primary air
pollution
Secondary air
pollution
O3, CH4
SMOG !
Emissions:
anthropogenic / biogenic
Deposition/Acidification/
Eutrophication

## Slide 3
Traffic-related VOC reduction
Mcdonalds et al., 2018, Science
Emission Trends in the South Coast Air Basin
Parrish et al., (2016)

## Slide 4: limonene
Coggon et al., PNAS2021
Gkatzelis et al., 2020, ES&T
12 Sept 2024

## Slide 5: Biogenic vs. vcp limonene
+ Stable Isotopes ?
(+) Limonene | (-) Limonene
shampoos, shower gels, scrubs | slash, loblolly pine oils
96-99% | ~100%
courtesy Shan Gu (Celia Faiola group, UCIrvine)
Enantiomer studies
- Quantitatively estimate of the relative contribution from biogenic vs. VCP sources
12 Sept 2024

## Slide 6
Isotopic signature of the sources
Notes: Limonene in the atmosphere

## Slide 7
Specific isotopic fractionation during reaction

## Slide 8
Isotopic hydrocarbon clock

## Slide 9: Objectives
Analyze source specific stable carbon isotope ratios of
biogenic and VCP limonene
  Methodology development for sampling limonene emissions from care and cleaning products as well as from trees in a simulation plant chamber
  TD-2D-GC-IRMS method development for limonene d13C measurements (limonene standards)
  Compound specific d13C measurements of biogenic vs. VCP limonene

## Slide 10: TD-2DGC-IRMS Measurement technique

## Slide 11: Quality Control of the Heart Cut TD-2DGC-IRMS measurements
Compound | δ 13C (‰) /Method | 
 | TD-2DGC-IRMS (n=25) | EA-IRMS (n=8)
(-)-limonene | -33,0 ± 0,5 | -33,7 ± 0,1
(+)-limonene | -30,0 ± 0,7 | -30,2 ± 0,1

## Slide 12: Standard samples for method development
12 Sept 2024

## Slide 13
ON/OFF Ventil
TENAX Tube
ON/OFF Ventil
Synth Air
90°C
Sampling VCP limonene from gas mouse

## Slide 14: Sampling of real plant emissions at SAPHIR PLUS
Sampling Flow Control by MFC
12 Sept 2024
Quick Sample Change

## Slide 15
Results
Essential oils
Care products
Trees
Latitude
Notes: Latitude

## Slide 16
Results – emission from trees
  Isotopic ratios of isoprene emissions - only one study (Sharkey et.al 1991) – 2 ‰ more negative than plant material
  Isotopic ratios of bulk plant material of conifer wood from -27.3 to - 24.4 per mil

## Slide 17: summary
TD-2DGC-IRMS method development
Sampling
methodology
development
Limonene in biogenic emissions lighter than plant material
Higher d13C values –
reactions by industrial processing
d13C / ‰
Latitude
d13C measurements of biogenic vs. VCP limonene

## Slide 18: Thank you for your kind attention

## Slide 19
Steps for production of industrial limonene
Collecting of Citrus peels and waste
Ectraction
Cold pressing
Distilation
Solvent exctraction
Purification and isolation
Concentration
Formulation and packiging
Chemical reactions
Enrichment in C13
Notes: Enrichment in C13

## Slide 20
Pseudo first order reaction rate:
(1)
(2)
Isotopic Fractionation
Products
Products

## Slide 21
Toluene + OH
Irei et al., 2011
X
Toluene
Y
∙ OH
Changing of δ13C during the reaction
δ13C
δ13C
δ13Ct >> 0
δ13Ct = 0
KIE
δ13Ct >> 0
δ13Ct > 0
Products
Reactants
Notes: To illustrate the Rayleigh fractionation, I’ve picked a plot from the Irei et al. study on the toluene oxidation by OH.
X is toluene and Y is OH. The isotopes of interest are C-12 and C-13.
You see the δ^13C evolution of toluene and the formed secondary particulate organic matter as a function of fraction of toluene during several oxidation experiments. The lines describe the calculated values, the symbols the observations. Since C-12 reacts slightly faster than C-13, toluene becomes enriched in C-13. At the reaction beginning, the products are depleted in C-13. Due to the further fractionation, the product delta value increases, too, reaching in the end the initial value of reactant. A comparison of predicted and observed δ^13C for toluene and the sum of all products clearly demonstrates a perfect agreement. This demonstrates that the carbon fractionation occurred in the initial reaction step

## Slide 22
Compound Specific Isotopic Analyses
OH addition
channel
H abstraction
channel
=6.31‰
=2.67‰
=6.31‰

## Slide 23
First- vs. Later-Generation Products
=6.31‰
- Nopinone -first-generation
product
- Acetone - later-generation products
Fisseha et al. JGR 2009
Notes: Finally, isotopic measurements make possible differentiating among first- and later-generation products.
Fiseha et al. measured the temporal evolution of isotope ratios in products of β-pinene ozonolysis. Nopinone shows the expected increasing trend for a first-generation product. Contrarily, acetone, which likely arises during the stepwise thermal desorption of high molecular weight compounds, becomes lighter during the reaction, which is an evidence that these compounds belong to later generations.

## Slide 24
Thermal Desorption - Gas Chromatography - Isotope Ratio Mass Spectrometry (TD-GC-IRMS) with temperature-controlled reaction chamber
Notes: Rtx-1301
Rtx-1701
Since our goal is to optimally separate complex mixtures, we plan to use 2D-GC. We intend to test different GC column pairs to cover a broad range of selectivity. Therefore, we introduce an additional cryotrap between the columns. The additional cryo-trapping unit allow for detailed investigations of different time intervals of the reaction. Fractions of the first column eluent, containing targeted analytes will be focused on this interface, to be injected onto the second column for a base line separation. GC operating conditions such as the temperature program and GC-column used will be optimized.
The GC is equipped with two columns with different polarities. The first very low polar column, which is connected to the FID, helps us to determine the retention times of the compounds of interests. The second column should improve resolution and selectivity for the polar compounds.

## Slide 26
Isotopic fractionation

## Slide 27
Kinetic Isotope Effect (KIE)
Piansawan et al., 2017
Piansawan et al., 2017

## Slide 28
Isotopic fractionation

## Slide 29: First results
(-)-Limonene
(+)-Limonene
Chromatogram of rush shower scrub sample from
gas mouse
Chromatogram of
spruce sample from
Saphir Plus
Notes: δ13C [‰]

## Slide 30: Sampling of real plant emissions at SAPHIR PLUS
12 Sept 2024

## Slide 31: method Adaption – 2DGC – heart cut
1) Transfer
2) Trapping
3) Sepparation
Trapping
RT Limonene
FID Chormatogram
-(-)Limonene Standard
Transfer
Sepparation
Notes: enlarge

## Slide 32: Results Limonen Standard
IRMS Chromatogram
Ref. Peaks
Ref. Peaks
-(-)Limonene -26,47‰
Notes: enlarge

## Slide 33: Results Dishwashing liquid
cutting window
Limonene -28,66‰
IRMS Chromatogram
FID Chromatogram
β-Pinen
Notes: enlarge

## Slide 34: Results Limonene Standard
(-)-Limonene
(+)-Limonene
(-)-Limonene
(-)-Limonene
(+)-Limonene
Col 2
RTX 1701
30 m length, 0.32 mm i.d.,
0.25 μm film thickness)
Col 2
Supelco Astec Chiraldex B-PM
30 m length, 0.25mm i.d.,
0.12 μm film thickness
Col 2
Supelco Astec Chiraldex B-DM
50 m length, 0.25mm i.d.,
0.12 μm film thickness

## Slide 35: appendices

## Slide 36: appendices
overlay MSD-chromatogram heart cutting GC window 8.0 min to 14.0 min
overlay MSD-chromatogram heart cutting GC window 9.8 min to 12.0 min

## Slide 37: appendices
cutting window
Limonene -28,660‰
IRMS Chromatogram
FID Chromatogram
β-Pinen