## Slide 1: Search for Permanent Electric Dipole Moments (Proposal for the 1st half of 2015)
December 15, 2014 Frank Rathmann on behalf of JEDI
1st Meeting of the COSY Beam Advisory Committee (CBAC)

## Slide 2: Outline
Introduction
Recent Achievements
  Spin coherence time
  Spin tune measurement
  Commissioning of RF Wien filter
  Study of machine imperfections
Proposed studies 1st half of 2015

## Slide 3: Preamble: The burning questions?
Why do we observe matter and almost no antimatter if we believe there is a symmetry between the two in the universe?
What is this "dark matter" that we can't see that has visible gravitational effects in the cosmos?
Why can't the Standard Model predict a particle's mass?
Are quarks and leptons actually fundamental, or made up of even more fundamental particles?
Why are there exactly three generations of quarks and leptons? How does gravity fit into all of this?
From http://particleadventure.org/beyond_start.html

## Slide 4: Physics: Observed Baryon Asymmetry
Carina Nebula: Largest-seen star-birth regions in the galaxy
Observed |  | WMAP+COBE (2003)
SM exp. |  | 
Observed |  | WMAP+COBE (2003)
SM exp. |  | 
Mystery of missing antimatter addresses the puzzle of our existence
Why this strange number? Why not zero?

## Slide 5
Charge symmetric  No EDM ()
Do particles (e.g., electron, nucleon) have an EDM?
: MDM
: EDM
Physics: Fundamental Particles

## Slide 6
Permanent EDMs violate P and T.
Assuming CPT to hold, CP violated also.
Not Charge symmetric
(aligned w/ spin)
EDMs: Discrete Symmetries
Notes: 6
6

## Slide 7: Introduction: Why charged particle EDMs?
No direct measurements of charged hadrons EDMs
Potentially higher sensitivity than neutrons
  longer life time
  more stored polarized protons/deuterons
  larger electric fields
Approach complimentary to neutron EDM
access to
EDM of a single particle not sufficient to identify CP-violating source
New approach, with potentially higher sensitivity

## Slide 8
For transverse electric and magnetic fields in a ring, the
anomalous spin precession is described by Thomas-BMT equation:
Magic condition: Spin along momentum vector
For any sign of , in a combined electric and magnetic machine
, where and
For (protons) in an all electric ring
(magic)
Concept: Frozen spin Method
 Magic rings to measure EDMs of free charge particles

## Slide 9
Place particles in a storage ring
Align spin along momentum („freeze“ horizontal spin precession)
Search for time development of vertical polarization
Concept: Rings for EDM searches
New Method to measure EDMs of free charged particles:
Magic rings with spin frozen along momentum
Notes: 9
9

## Slide 10: Outline
Introduction
Recent Achievements
  Spin coherence time
  Spin tune measurement
  Commissioning of RF Wien filter
  Study of machine imperfections
Proposed studies 1st half of 2015

## Slide 11
turn spin
free precession
polarimeter
Spin coherence time: Experimental investigation
Vertically polarized deuterons stored in COSY at .
The polarization is flipped into horizontal plane with RF solenoid, takes .
Beam slowly extracted on Carbon target with ramped bump or by heating the beam.
Horizontal (in-plane) polarization determined from Up-Do asymmetry in the detector.
Experimental investigations of SCT in storage ring: Keep track of the event time and revolution time in each turn during a cycle of a few hundred seconds.

## Slide 12
Spin coherence time: Beam setups
Two different beam setups were used:
  Large , and
  large horizontal beam emittance.

## Slide 13
Polarimeter: Experimental investigation of SCT
where
D, and

## Slide 14
Polarimeter: Determination of SCT
One observes the experimental decay of the asymmetry as function of time, .

## Slide 15
Polarimeter: Optimization of SCT
Using sextupole magnets in the machine, higher order effects can be corrected, and the SCT is substantially improved

## Slide 16: SCT: Chromaticity studies
Maximal horizontal polarization lifetimes from scans with a horizontally wide or a long beam agree well with the lines of .
Chromaticity defines the tune change with respect to momentum deviation
Strong connection between and observed.
COSY Infinity based model predicts negative natural chromaticities and .
Measured natural chromaticity: and .
Crucial for achieving a large is careful adjustment of .

## Slide 17: SCT: Optimization
Measurements of the horizontal polarization lifetime as a function of the strength of the MXG sextupole family with MXS set to and MXL set to of power supply full scale.
Excellent progress towards the SCT goal for pEDM: s

## Slide 18: Spin tune: How to find ?
Spin tune : Number of spin precessions per turn
Detector rate is , while one hit in detector per beam revolutions.
Solution: Map all events into first spin oscillation period.

## Slide 19
Spin tune: How to find ?
Of course, this only works when was correct

## Slide 20
Spin tune: Scan of
Pick with maximum amplitude of asymmetry.

## Slide 21
Spin tune: D
Spin tune determined to in 2 s. in cycle at is determined to . (publication in prep.)

## Slide 22: New physics: Option for polarized antiprotons
JEDI is capable to determine the spin tune (number of spin revolutions per turn) of deuterons in COSY with a precision of .
With a suitable magnetic storage ring (ESR (GSI), AD (CERN)) with cw protons and CCW antiprotons, the ratio could be measured to similar precision.

## Slide 23: RF Wien Filter: Prototype commissioning
Precursor EDM concept: Use RF Wien filter to accumulate EDM signal
Insert RF-dipole into ceramic chamber

## Slide 24: RF Wien Filter: Field calculations
Main field component
at ,
Main field component
at ,
Integral compensation of Lorentz force at

## Slide 25
    RF Wien Filter: Resonance condition
Deuterons at 970 MeV/c: ; ;
,
Frequency range RF Wien filter

## Slide 26
    RF Wien Filter: Measurement of Resonance Strengths
Continuous polarimetry: Fixed frequency scans for resonance determination
Damping due to decoherence
Cross-ratio of UD-asymmetries used.
Minimum vertical polarization oscillation frequency gives resonance strength:
871.4276
871.4276
871.4276
0.20
0.25
0.30
0.35

## Slide 27
    RF Wien Filter: Preliminary Results
RF solenoid:
RF Wien filter:
RF dipole:
M.A. Leonova et al., contribution to Spin 2008
From driven vertical oscillation at fixed frequency
From froissart-Stora scans
RF 𝐄×𝐁 Wien filter performs like an RF solenoid

## Slide 28: RF Wien filter: Strip line design
Strip line design provides
Strip-line RF 𝐄×𝐁 Wien filter available 2nd half of 2015.
Device will be installed in PAX low- section
BPM
(Rogowski coil)
Ferrit cage
Copper
electrodes
Mechanical support
from exit flange
RF
feedthrough
Device rotatable by in situ

## Slide 29: Systematic study: Machine imperfections using two straight section solenoids
Idea: The precise determination of the spin tune can be exploited to map out the imperfections of COSY.
COSY provides two solenoids in opposite straight sections:
  one of the compensation solenoids of the 70 kV cooler: ,
  The main solenoid of the 2 MV cooler: .
Both are available dynamically in the cycle, i.e., their strength can be adjusted on flattop.
Systematic effects from machine imperfections limit the achievable precision in a precuror experiment using an RF Wien filter.

## Slide 30: Systematic study: Simulation of one imperfection kick for deuterons at MeV/c
Ideal machine with vanishing static imperfections: Saddle point at the origin
sea level at
Intrinsic imperfection kick shifts saddle point away from origin
Location of imperfection:

## Slide 31: Systematic study: Thomas-BMT eq. in magnetic machine
, and
BMT for magnetic machine with
Interaction of EDM with motional E-field ) tilts stable spin axis:
Goal: explore dynamics and systematic limitations of EDM searches in magnetic ring
Misalignment of magnetic elements produces in-plane imperfection magnetic fields:
Non-vanishing and generate background to the EDM-signal of an ideal imperfection-free machine (, and ).
The challenge is to control this background:
An accuracy amounts to a sensitivity .

## Slide 32: Systematic study: Imperfection measurement
Probing the in-plane imperfection fields by introducing artificial imperfections and looking for the spin tune response
The values of , and depend of spin kicks in non-vertical imperfection fields in the arcs spin tune perturbed:
Use the compensation and e-cooler solenoids in straight sections (points 1 and 2): spin kicks and .
Probe the in-plane imperfection fields by introducing well-known artificial imperfections and .

## Slide 33
Systematic study: Measurement of spin tune shift
Take multiple measurements with different , , build a spin tune map

## Slide 34
Systematic study: Mapping imperfections
Map translated to
From the map taken on 18+19.09.2014, with the baseline spin tune at , one finds: .
Fit map to locate saddle point

## Slide 35
Systematic study: Mapping imperfections
Map translated to
New technique allows one to experimentally reconstruct the components of the spin closed orbit in a storage ring with unprededented precision (not achievable from polarization measurements alone).
Extremum of spin tune map is saddle point at .
Once baseline spin tune determined, are only fit parameters.
Solenoids only are not sensitive to (static WF with and ).

## Slide 36: Outline
Introduction
Recent Achievements
  Spin coherence time
  Spin tune measurement
  Commissioning of RF Wien filter
  Study of machine imperfections
Proposed studies 1st half of 2015

## Slide 37
January
July
December
5 weeks + 1MD
(only b beam)
~ 5 weeks +1 MD
(d and p beam)
new RF Wien filter
4. RF Wien filter at 630 kHz
3. Quartered Rogowski coil
2. EDDA fiber target
    1. Explore d beams at other energies with EDDA
Beam request: JEDI studies with beam in 2015
7. Beam extraction at EDDA target with ANKE cluster or WASA pellet
6. Study effect of a variation of the electron cooler beam current on
5. SCT studies with straight section sextupoles

## Slide 38: Beam Request: 1. Exploring other energies with EDDA
Up to now spin coherence times were only studied with deuterons at ().
There are indications that the damping of RF-driven spin oscillations depends on the beam energy and on the harmonic (next slides).
  JEDI would like to explore higher energies with EDDA, where deuteron analyzing powers are known to be sizeable.
pC analyzing power
N.E. Cheung et al., NIM A 363, 561 (1995)
dC analyzing power
V. P. Ladygin et al., NIM A 404, 129 (1998)

## Slide 39: Beam Request item1: Harmonic dependence of damping time of RF solenoid driven vertical oscillations
Spin coherence time (s)
235 MeV
Beam energy (MeV)
Observation of enhancements of damping time for p and d requires more flexible polarimeter
Theory: N.N.Nikolaev
Observed oscillating , driven by RF solenoid at different harmonics

## Slide 40: Beam Request: 2. EDDA fiber target
During the studies carried out so far, the beam was extracted using electro-magnetic fields which have an influence on the spin precession.
Avoided using a fiber target which runs through the beam,
Offers possibility to study polarization and spin tune as function of position in the beam.

## Slide 41: Beam Request: 3. Quartered Rogowski coil
For bunched beams, sum signal of Rogowski coil can be used as a beam current monitor.
Installed in ANKE target chamber
Readout
Rogowski coil
BCT
Bunched beam
Integral signal measures beam current
Quadrant signals sensitive to position

## Slide 42: Beam Request: 3. Quartered Rogowski coil
EDM experiments use bunched beams:
Rogowski coil system well-suited.
Small size allows for flexible installation ( Stripline RF Wien filter)
Quadrant signals of Rogowski coil sensitive to beam position.
Tests will be carried out parasitically.
Integral signal measures beam current
Quadrant signals sensitive to position

## Slide 43: Beam Request: 4. RF Wien filter at
The commissioning of the RF Wien filter was done at the harmonic ()
We would like to extended the studies to the harmonic .

## Slide 44: Beam Request: 5. SCT studies with the straight section sextupole
In the past beam times, the influence of arc sextupoles families MXS, MXG, and MXL on SCT was studied.
We would like to use the sextupoles in the straight sections as well to suppress third order field contributions.

## Slide 45: Beam Request: 6. Study effect of a variation of the electron cooler beam current on
Up to now the electron cooler beam was switched off during the idle precession of spins in the horizontal plane.
We propose to study the influence of
the electron cooler beam current on .
Non-linear fields of the electron beam affect by additional spin kicks.
  Magnitude of spin kicks depends on particle position inside electron beam.
Better phase-space mixing could lengthen .
  Interplay of beam cooling and heating by intra-beam scattering beam.
Measurements should be done with continuous cooling
  Equilibrium phase-space distribution.
  Adjust cooling rate during cycle by changing electron beam current to match the intra-beam heating rate.

## Slide 46: Beam Request: 7. Beam extraction onto EDDA target with ANKE cluster or WASA pellet
Extraction procedures of JEDI and srEDM experiments up to now only included ramping and white-noise heating the beam to produce interactions with the C target.
We would like to test beam extraction using an internal target (either ANKE cluster or WASA pellet target)

## Slide 47: JEDI Beam Request: 1st half of 2015
We request in total 5 weeks of beam time for the activities:
  Explore other energies with EDDA
  EDDA fiber target
  Quartered Rogowski coil at ANKE chamber
  RF Wien filter at 630 kHz
  SCT studies with straight section sextupoles
  Study effect of a variation of the electron cooler beam current on
  Beam extraction onto EDDA target with ANKE cluster or WASA pellet
preceeded by 1 MD week.
Investigations require time consuming machine tuning. Therefore, beam time should be scheduled as single block.

## Slide 48
Jülich Electric Dipole Moment Investigations:
100 members (Aachen, Dubna, Ferrara, Indiana, Ithaca, Jülich, Krakau, Michigan, Minsk, Novosibirsk, St. Petersburg, Stockholm, Tbilisi, …)
JEDI Collaboration
Submitted Design Study to European Union (1.9.2014):
  Novel precision storage rings for Electric Dipole Moment searches
JEDI proposals:
Visit our website at
http://collaborations.fz-juelich.de/ikp/jedi/documents/proposals.shtml
Thanks go to the dedicated IKP crew, our collaborators, and the students:
  Artem, Dennis, Fabian, Fabian, Greta, Jamal, Marcel, Nils, Paul, Sebastian, Stas, and Zara

## Slide 49: Publications
Experiment:
N.P.M. Brantjes et al., Correcting systematic errors in high-sensitivity deuteron polarization measurements, Nucl. Instrum. Meth. A664, 49 (2012), DOI: 10.1016/j.nima.2011.09.055
Z. Bagdasarian et al., Measuring the Polarization of a Rapidly Precessing Deuteron Beam, Phys. Rev. ST Accel. Beams 17 (2014) 052803, DOI: 10.1103/PhysRevSTAB.17.052803.
F. Rathmann et al. [JEDI and srEDM Collaborations], Search for electric dipole moments of light ions in storage rings, Phys. Part. Nucl. 45 (2014) 229, DOI: 10.1134/S1063779614010869.
Frank Rathmann, Artem Saleev, N.N. Nikolaev [JEDI and srEDM Collaborations], The search for electric dipole moments of light ions in storage rings J. Phys. Conf. Ser. 447 (2013) 012011, DOI: 10.1088/1742-6596/447/1/012011.
P. Benati et al., Synchrotron oscillation effects on an rf-solenoid spin resonance, Phys. Rev. ST Accel. Beams 15 (2012) 124202, DOI: 10.1103/PhysRevSTAB.15.124202.
A. Lehrach, B. Lorentz, W. Morse, N.N. Nikolaev, F. Rathmann, Precursor Experiments to Search for Permanent Electric Dipole Moments (EDMs) of Protons and Deuterons at COSY, e-Print: arXiv:1201.5773 (2012).
Theory:
J. Bsaisou, J. de Vries, C. Hanhart, S. Liebig, Ulf-G. Meißner, D. Minossi, A. Nogga, A. Wirzba, Nuclear Electric Dipole Moments in Chiral Effective Field Theory, e-Print: arXiv:1411.5804.