## Slide 1: Medical Radionuclide Production at HZDR
Nadiya Zhutova, Institute of Radiopharmaceutical Cancer Research
Georgian-German Science Bridge, September 7th to 12th 2026
Notes: name, working at HZDR that prof. Schmidt presented earlier today. Happy to be here in Tbilisi and glad to present my institute today.

## Slide 2: Institute of Radiopharmaceutical Cancer Research
Radioimmunology
Positron Emission Tomography
Nano-Microsystems for Life Sciences
Radiopharmaceutical and Chemical Biology
Experimental Neurooncological Radiopharmacy
Medicinal Radiochemistry
Targetry, Target Chemistry and Radiopharmacy
Departments

## Slide 3: Institute of Radiopharmaceutical Cancer Research
Radioimmunology
Positron Emission Tomography
Nano-Microsystems for Life Sciences
Radiopharmaceutical and Chemical Biology
Experimental Neurooncological Radiopharmacy
Medicinal Radiochemistry
Targetry, Target Chemistry and Radiopharmacy
Departments
Radionuclide production
Radiochemistry
Development of Radiopharmaceuticals
Innovative Test Systems and Models
GMP
Innovative Test Systems and Models

## Slide 4: Institute of Radiopharmaceutical Cancer Research
Radioimmunology
Positron Emission Tomography
Nano-Microsystems for Life Sciences
Radiopharmaceutical and Chemical Biology
Experimental Neurooncological Radiopharmacy
Medicinal Radiochemistry
Targetry, Target Chemistry and Radiopharmacy
Departments

## Slide 5: Institute of Radiopharmaceutical Cancer Research
Radioimmunology
Positron Emission Tomography
Nano-Microsystems for Life Sciences
Radiopharmaceutical and Chemical Biology
Experimental Neurooncological Radiopharmacy
Medicinal Radiochemistry
Targetry, Target Chemistry and Radiopharmacy
Departments

## Slide 6: Radiopharmaceuticals
What is it and how does it work?
A radiopharmaceutical is a drug that specifically targets certain cells or functions in the body and uses radioactive isotopes for diagnostics or therapy.
Fig. from: [1] Kostelnik, T.I. and Orvig, C., Chem. Rev. 2019, 119, 2, 902.
Diagnostics & Therapeutics
© A.Vargas/IAEA

## Slide 7: Radiopharmaceuticals
A radiopharmaceutical is a drug that specifically targets certain cells or functions in the body and uses radioactive isotopes for diagnostics or therapy.
© Kostelnik, T.I. and Orvig, C., Chem. Rev. 2019, 119, 2, 902.
Diagnostics & Therapeutics
© A.Vargas/IAEA
© Clarity Pharmaceuticals, Quarterly Activity Report, March 2026
What is it and how does it work?

## Slide 8: Radiopharmaceuticals
© Kostelnik, T.I. and Orvig, C., Chem. Rev. 2019, 119, 2, 902.
Diagnostics & Therapeutics
© Clarity Pharmaceuticals, Quarterly Activity Report, March 2026
True theranostic matched pairs:
    43/44Sc/47Sc
    61/64Cu/67Cu
    86Y/90Y
    123I/131I
    152/155Tb/149/161Tb
    203Pb/212Pb
What is it and how does it work?

## Slide 9: Theranostics
When Diagnostics and Therapy unite
© Kostelnik, T.I. and Orvig, C., Chem. Rev. 2019, 119, 2, 902.
© Clarity Pharmaceuticals, Quarterly Activity Report, March 2026
True theranostic matched pairs:
    43/44Sc/47Sc
    61/64Cu/67Cu
    86Y/90Y
    123I/131I
    152/155Tb/149/161Tb
    203Pb/212Pb
Task: get the right radionuclide, in the right purity and amount
Diagnostics & Therapeutics

## Slide 10: Production of Medical Radionuclides
What are the ways?
Accelerator produced
Generator
produced
Reactor produced
PERTECTOR Mo-99/Tc-99m radionuclide generator © by ROTOP
Examples:
68Ge/68Ga, 99Mo/99mTc
RA-06 Nuclear Reactor, Argentina (Fig. S. A. Brühlmann)
Examples:
161Tb, 177Lu
TR-FLEX Cyclotron (Fig. M. Wendler, HZDR)
Examples: 43/44Sc, 61/64Cu

## Slide 11: Production of Medical Radionuclides
What are the ways?
Accelerator produced
Generator
produced
Reactor produced
PERTECTOR Mo-99/Tc-99m radionuclide generator © by ROTOP
Examples:
68Ge/68Ga, 99Mo/99mTc
RA-06 Nuclear Reactor, Argentina (Fig. S. A. Brühlmann)
Examples:
161Tb, 177Lu
TR-FLEX Cyclotron (Fig. M. Wendler, HZDR)
Examples: 43/44Sc, 61/64Cu
Notes: In cyclotrone we accelerate hydrogen ions, that are later extracted as protons

## Slide 12: Cyclotron-Based Production of Medical Radionuclides
What are the steps to follow?
Selection of the Nuclear Reaction
Target Preparation
    Solid, Liquid or Gas Targets
Target Irradiation (and Parameters Optimization)
Purification – radionuclide extraction
Target Recycling

## Slide 13: Cyclotron-Based Production of Medical Radionuclides
Choose your superhero
True theranostic matched pairs:
    43/44Sc/47Sc
    61/64Cu/67Cu
    86Y/90Y
    123I/131I
    152/155Tb/149/161Tb
    203Pb/212Pb
Diagnostics Therapeutics

## Slide 14: Cyclotron-Based Production of Medical Radionuclides
Choose your superhero
Diagnostics Therapeutics
CopperNostics@HZDR
Same element, different applications!

## Slide 15: Cyclotron-Based Production of Medical Radionuclides
Choose your superhero
Diagnostics Therapeutics
CopperNostics@HZDR
Same element, different applications!

## Slide 16: Nuclear Reaction Selection
The 70Zn(p,α)67Cu nuclear reaction

## Slide 17: Target Preparation
Target Electrodeposition:
Starting from fresh or recycled 70Zn
Electrodeposition onto gold or silver backing
Solid Targets - 67Cu
Electrodeposited 70Zn target from fresh
[70Zn]ZnSO4 solutions onto gold.
Electrodeposited 70Zn target from recycled
[70Zn]ZnSO4 solutions onto silver.
Brühlmann, S.A., et al. Pharmaceuticals 2023, 16, 314.
Electroplating device used for 70Zn electrodeposition.
Notes: 70Zn 97.5% enrichment

## Slide 18: Target Irradiation
The 70Zn(p,𝛼)67Cu Reaction:
Irradiation energy below 17 MeV to reduce 67Ga co-production
Water cooled energy degrader developed in-house
Influence of the projectile energy on the nuclear reaction
Relevant cross sections weighted for the target abundancy.
Brühlmann, S.A., et al. Radiochimica Acta 2026: 2, 114.
Notes: ⁶⁷Ga has a half-life of about 78.3 hours. Vertical dashed line- incident proton energy, dotted lines – proton exiting energies

## Slide 19: Target Irradiation
Solid targets: thermal input
Target scheme including water and helium cooling
Water Cooling
Helium Cooling
Gold/Silver Backing
Zinc Target
Proton Beam
Gold Backing
Zinc Target
    Melting Point of Zinc: 420°C!
Melted zinc targets with a gold backing
Temperature profile of a target when using different beam currents
Notes: we irradiate @ 60 micro amps

## Slide 20: Radiochemical Purification
Radionuclide extraction – 67Cu
8-15 h decay time after irradiation (decay of shorter-lived radionuclides)
Two separation columns: AG-1x8+TK221 and TK201
Overall Efficiency: above 75%
Brühlmann, S.A., et al. EJNMMI radiopharm. chem. 2024, 9, 3.
2-Step Purification Scheme for 67Cu
Purification Module for 67Cu

## Slide 21: Product Characterization – Quality Control
The radionuclidic purity (RNP) is the ratio of the activity of the main product and the total activity of the sample, that is, the activity of the product and all side products also present:
This parameter is usually requested to be over 95% or higher, depending on the radionuclide. It can be determined by performing gamma-spectroscopic measurements.
Radionuclidic Purity – Radioactive Impurities
RNP = 100 %
RNP < 100 %
Notes: as well - (apparent) molar activity to see stable impurities (ICP-MS)
test radiolabelling and verification by radio-TLC

## Slide 22: Product Characterization
Radionuclidic Purity – 67Cu
Gamma-spectroscopy of the [67Cu]CuCl2 solution (14 h after irradiation).
Main radioimpurities: 61Cu and 64Cu (shorter half-lives than 67Cu) The RNP increases with the time
>99 % 18 h after irradiation, >99.5 % 24 h after irradiation
Brühlmann, S.A., et al. Pharmaceuticals 2023, 16, 314.
Notes: 511 keV – electron-positron annhilation peak, ⁶⁷Ga has a half-life of about 78.3 hours
as well - (apparent) molar activity to see stable impurities (ICP-MS)
test radiolabelling and verification by radio-TLC

## Slide 23: Recovery of Target Material
Precipitation of [70Zn]Zn(OH)2:
Addition of 6 M NaOH until pH 9
Centrifugation, separation of the supernatant, and subsequent washing (x5)
(Drying of the precipitate and annealing)
Recovered material used for a new round of electroplating
Target recycling – 70Zn for 67Cu
Precipitated and centrifugated [70Zn]Zn(OH)2.
Drying of the [70Zn]Zn(OH)2.
[70Zn]ZnO recovered after annealing.
Brühlmann, S.A., et al. Pharmaceuticals 2023, 16, 314.

## Slide 24: Summary: Radionuclides produced at the HZDR
HZDR’s current radionuclide portfolio
PET Radionuclides: 11C, 18F, 61Cu, 64Cu, 89Zr & 133La
SPECT Radionuclides: 67Ga, 123I, 131Ba
β--emitting Radionuclides: 67Cu
Conversion and Auger Electron Emitters: 135La, 197(m)Hg

## Slide 25: GGSB – Internship at HZDR
Successful case
In March-April 2026 Mariam Kenkadze worked on the project
“Cyclotron Production and Radiolabeling Studies with 135La for PSMA radioligands”
Scheme of the 136Ba(p,2n)135La nuclear reaction
Results from Mariam’s internship were included in the article that is going to be published soon

## Slide 26: Thank you! გმადლობთ!
Institute of Radiopharmaceutical Cancer Research
Curious about an internship with us?
Send me an email: n.zhutova@hzdr.de
← or contact me on LinkedIn
Notes: გმადლობთ (pronounced roughly gmadlobt)