## Slide 1: Integrated Computing Architectures at FZJ
08.09.2026 | André Zambanini

## Slide 2: Integrated Computing Architectures
Semiconductors enable Future Computing architectures
  High integration, VLSI scalability
System integration of memristors, qubits, etc.
   Algorithms, hardware and physics co-design
System modeling of hardware implementations
   Application requirements and error mitigation / correction
Applications
Algorithms
Methods
…
Novel Devices
Qubit Memristor
…
Integrated Computing Architectures
Neuromorphic Computing
Quantum Computing
~60 people (staff, post-docs, PhDs)
Notes: Overlap between NC and QC

## Slide 3: Performance Scaling Limited by Memory?
How to overcome the memory limitations?
Energy Footprint of Computing vs. Data Movement
Scaling of Computing vs. Memory Bandwidth
Gholami A, et al. „AI and Memory Wall“, arXiv (2024). [https://arxiv.org/abs/2403.14123]
Horowitz, M., “Computing’s Energy Problem (and what we can do about it)”, IEEE ISSCC, 2014
BIOLOGICAL INSPIRATION: Memory Integral Part of the Computing
NC!
Neuromorphic Computing

## Slide 4: Focus Topics in Neuromorphic Computing
Crossbar Arrays
Oscillatory Neural Networks
Edge AI Applications
Neuromorphic Computing

## Slide 5: Crossbar Arrays used for Computing in Memory
Crossbar arrays are the basis for computing in memory (CIM)
Memristors: non-volatile, high-density
Alternative nodes possible
System design important (network on chip, analog interconnects)
Crossbar Arrays
Oscillatory Neural Networks
Edge AI Applications
ORCA / D1: Integrated Memristors
Neural Network
Neuromorphic Computing

## Slide 6: NEUROTEC II: Demonstrator System
Platform for Multiple Bio-Inspired Computing Paradigms
Versatile Demonstration Vehicle
4 programmable memristive crossbar arrays with
> 65.000 memristors co-integrated (post-processing)
2560 8-bit ADC and 4-bit DAC integrated
Automatic memristor control enabled
Flexible Interfaces
Network on Chip (NoC)
Chipbridge for direct NoC access
Standard JTAG programming interface
 Different bio-inspired computing paradigms
Concept developed in close collaboration within FZJ
Crossbar Arrays
Oscillatory Neural Networks
Edge AI Applications

## Slide 7: NEUROTEC II: Demonstrator System
Platform for Multiple Bio-Inspired Computing Paradigms
Versatile Demonstration Vehicle
4 programmable memristive crossbar arrays with
> 65.000 memristors co-integrated (post-processing)
2560 8-bit ADC and 4-bit DAC integrated
Automatic memristor control enabled
Flexible Interfaces
Network on Chip (NoC)
Chipbridge for direct NoC access
Standard JTAG programming interface
 Different bio-inspired computing paradigms
Concept developed in close collaboration within FZJ
Crossbar Arrays
Oscillatory Neural Networks
Edge AI Applications
900 µm
750 µm
128 8-bit ADCs
Nominal: 200 MSample/s

## Slide 8: NEUROTEC II: Memristor Integration
State-of-the-Art Memristor Integration
Fab-level RRAM: binary memory with controller  no access to the device
Research-level: memristor off-chip, wirebonding at best  scale-up issues and strong parasitic effects
Goal: True Memristor Integration into/onto CMOS
Robust 180 nm CMOS for prove of principle
Modern 28 nm CMOS for scalable and high-performance
  Issues: full wafer (too)expensive, MPW chiplets small and fully processed, copper complicated in clean rooms, …  tricky integration, but doable
Outlook: integration into BEOL on 22 nm FD-SOI planned
Crossbar Arrays
Oscillatory Neural Networks
Edge AI Applications
Memristor deposition by PGI-7 & HNF @ FZJ

## Slide 9: The Magic Lies in the Coupling
Chip Layout
1.4 mm
1.0 mm
SRAM
JTAG RISC-V
PLL 2
PLL 1
PLL 3
PLL 5
PLL 4
PLL 6
PLL 7
Crossbar Arrays
Oscillatory Neural Networks
Edge AI Applications
Neuromorphic Computing
Brain-inspired computing: processing based on overlay of oscillations
Coupling of oscillators
Information is in the phase
Analog and mixed-signal circuits for Pattern Recognition

## Slide 10: Coupled Oscillator System
Crossbar Arrays
Oscillatory Neural Networks
Edge AI Applications
Neuromorphic Computing
architecture
Configurable coupling
S.Y. Nayaz, A. Ashok, et.al, „Scalable 28nm IC implementation of coupled oscillator network featuring tunable topology and complexity“, https://arxiv.org/abs/2505.10248

## Slide 11: Edge AI Applications: Reuse of our Developments
Crossbar Arrays
Oscillatory Neural Networks
Edge AI Applications
Neuromorphic Computing
Applications, demo‘ing the potential of Edge AI,
e.g. Einstein Telescope
Low-energy, low-latency use cases
Goal: Systems with crossbars or ONNs
 Hardware Demonstrator
Online Noise Mitigation @ Einstein Telescope
Online Feature Detection @ Pierre Auger Observatory
Algorithm Development and On-Device Training

## Slide 12: Online Newtonian Noise Prediction for ET
Crossbar Arrays
Oscillatory Neural Networks
Edge AI Applications
Neuromorphic Computing
Seismic Sensor Network around Detector
 Enable noise prediction based on AI
Einstein Telescope Noise Impacts
 Low-freq. dominated by seismic noise
Binary Star System
When approaching: increasing frequency
(src: Wikimedia)
Multi-Messenger Observation
Gravitational waves can predict collision
 The earlier we get aware of an event, the more time we have to redirect other detectors
Goal: Online Newtonian Noise Mitigation
Real-time readout and data processing of sensor network
Complex transfer function for noise prediction
Approach: FPGA-based Neural Networks
In collaboration with:

## Slide 13: Integration with CMOS Electronics
Benefit From Existing Infrastructure To Scale Up
cryogenic electronics
qubit
CLASSICAL COMPUTER
100 mK
300 K
QUANTUM-CLASSICAL INTERFACE
QUANTUM PROCESSOR
OUR FOCUS AREA
Quantum Computing

## Slide 14: System Modelling, Design and algorithmics
schematic
CO-SIMULATION
MODELLING
SYSTEM DESIGN
electronic Architecture
Physics model
CSD Data
AUTOMATED TUNING
Geometric model
Automated Detection
MODELLING / SIMULATION
TRAINING / DETECTION
Quantum Computing

## Slide 15: Cryogenic Circuit Design and Measurement
CryogeniC Circuit design
Cryogenic MeasurementS
Schematic design
Test device SETUP
Cryo Setup
Verification Results
Implemented circuits
Quantum Computing

## Slide 16: Cryogenic Measurements
Inputs for a Cryo-PDK for 22 nm CMOS
Analyzer
Transistor Arrays
60 K Stage
300 K Stage
ID [a.u.]
7 K
7 K
Input Data for BSIM-IMG Based Modeling
done by AdMOS GmbH
Cryogenic Model Library
Short-Channel I-V-Curves [1]
DUT
The QSolid project acknowledges the support of the Federal Ministry of Education and Research (BMBF) within the framework program “Quantum technologies – from basic research to market” (Grant No. 13N16149).
Setup @ ICA | FZJ: Tmin ~ 7 K
Source: [2]
Related to DRD7.4a

## Slide 17: Summary
Integrated Computing Architectures
Neuromorphic Computing
Quantum Computing
Semiconductors Enable Future Computing Architectures
  High integration, VLSI scalability
System Integration of Memristors, Qubits, etc.
  Algorithms, hardware and physics co-design
System Modeling of Hardware Implementations
   Application requirements and error mitigation / correction
Notes: Overlap between NC and QC