## Slide 1: Seismic Signal Prediction from an Accelerometer Array towards Online Newtonian Noise MitigatioN BY FPGA
25-08-2026 | Elguja Abuladze
Master thesis Final
შოთა რუსთაველის საქართველოს ეროვნული სამეცნიერო ფონდის მხარდაჭერით [GHZ-25-005] / This work was supported by Shota Rustaveli National Science Foundation of Georgia (SRNSFG) [GHZ-25-005]

## Slide 2: background
Detection of gravitational waves using laser interferometry
Enables multimessenger observations of the universe
Significantly improved sensitivity compared to current detectors (LIGO/Virgo)
Limited by environmental noise sources (e.g., Seismic noise)
ET Pathfinder: experimental platform in Maastricht for development and validation of ET concepts
Einstein Telescope – What it is and how it works

## Slide 3: background
Combines observations from different types of signals(gravitational waves, electromagnetic radiation…)
Provides a more complete understanding of astrophysical events
Example: binary neutron star merger
  detected via gravitational waves (LIGO/Virgo)
  detected via gamma rays (Fermi)
Requires real-time detection and rapid communication to enable follow-up observations
Multimessenger

## Slide 4: background
  Advantages
  Real-time processing ( ~ 1ms @ 1000Hz)
  Low and deterministic latency
  Streaming, parallel, and pipelined processing
  Constraints
  Limited on-chip resources: BRAM, DSP, LUT, and FF
  Fixed-point quantization and hardware-aware model optimization
  Model architecture must be supported by the HLS toolchain
What changes due to FPGA

## Slide 5: Methodology
prediction of the target sensor from the others
Sensor arrays, as proxy measurements
CH N+1 | t-w |  | t-3 | t-2 | t-1
CH 1 |  | … |  |  | 
CH 2 |  | … |  |  | 
CH 3 |  | … |  |  | 
 | : |  | : | : | :
CH N |  | … |  |  | 
CNN
t
CH N + 1
Surrounding Sensors
(Channel per Axis)
Current Prediction
of Target Sensor
Window Size = w

## Slide 6: methodology
Correlation
SER
Frequency domain evaluation
Residual analysis
Model performance evaluation
Ratio between target-signal power and residual power, expressed in dB
Primary evaluation metric Higher SER indicates better reconstruction.
Time-domain and frequency-domain metrics are combined because no single metric fully describes reconstruction quality.

## Slide 7: methodology
Residual analysis

## Slide 8: Methodology
Datasets and preprocessing ETPF – Corridonia – Hi-Net
 | ETPF | Corridonia | Hi-Net
Dataset size | 30 hours + 8 days | ~ 2 hours | 12 hours
Sampling rate and Bit rate | 500 Hz, 24-bit resolution | 250 Hz, 20-bit resolution | 100 Hz, 27-bit resolution
Number of channels | 13 vertical | 5 three-axial sensors (15 channels) | 13 vertical

## Slide 9: Selected Model Architectures
Optuna selected different temporal windows and model depths for the two datasets
Model B
Input (signal)
(87, 12)
2x
Conv + BatchNorm+ ReLu + Dropout
Linear (32, 64)
Model A
Conv + BatchNorm+ ReLu + Dropout
Input (signal)
(240, 12)
Linear (16,256)
Hyperparameter | Search space
Window size | 64–300 samples*
Learning Rate | 5 × 10⁻⁵ – 10⁻³
Batch size | 1 – 128
Optimizer | Adam, RMSprop
Dropout | 0.0 – 0.6
Conv. Layers | 1 – 4
Channels | 4 – 256
Kernel size | 1 – 128
ReLU | True/False
Hidden | 4 – 256
Model A — optimized on ETPF
Model B — optimized on Corridonia
*sampling rate: 500 Hz

## Slide 10: Offline results - etpf
Primary evaluation dataset
Most model development and evaluation in this thesis is based on ETPF measurements.
Continuous, high-resolution recordings enable detailed analysis of seismic noise.
Measurements collected at ET Pathfinder provide an experimentally relevant environment for ET-related seismic studies.
The additional eight-day recording enables evaluation over changing long-term noise conditions.
We gratefully acknowledge the active collaboration of the ET Pathfinder team.

## Slide 11: Offline results - etpf
SER heatmap
Each cell represents a separately trained model; the main value is its SER.
Rows indicate target sensors; columns indicate the sensor removed from the inputs.
Diagonal cells represent nominal training with not any sensor removed.
Removing some sensors improves SER, showing that certain input channels can reduce prediction quality.
Colors are normalized per row; σ=0.11 values show the change relative to the nominal result and are comparable across rows.

## Slide 12: Fpga implementation
The model is constructed and trained in PyTorch.
The trained model can be exported to ONNX as a framework-independent representation.
The trained PyTorch model is converted directly using hls4ml.
hls4ml generates synthesizable HLS C++ code.
HLS synthesis converts the design into RTL for FPGA implementation.
Neural-network deployment workflow
PyTorch
hls4ml
ONNX
HLS C++
RTL

## Slide 13: Fpga implementation
Footprints
Input channels | BRAM (18K) | DSP | FF (K) | LUT (K)
1 | 402 | 71 | 91 | 73
4 | 409 | 70 | 95 | 73
8 | 417 | 70 | 101 | 76
11 | 422 | 71 | 105 | 77
13 | 426 | 71 | 108 | 78
22 | 444 | 73 | 119 | 82
Resource Utilization for Model B (Model A pending due to ONNX issues)
ZCU216 | 2160 | 4272 | 850 | 425
Reducing the number of input channels has little effect on DSP utilization.
Removing less informative channels reduces BRAM, FF, and LUT utilization.
Performance remains nearly unchanged down to eight input channels, but decreases significantly below this point.
The estimated inference latency remains approximately 0.464 ms for all channel configurations.
The estimated neural-network-core latency is below the 1 ms sampling interval, indicating computational feasibility at 1 kHz.
The HLS-estimated clock period ranges from 3.61 to 4.63 ns
the target period is 5 ns.

## Slide 14: Fpga implementation
cocotb

## Slide 15: Wiener FILTER
The Wiener filter reconstructs the target signal from correlated witness signals using an optimal linear filter that minimizes the mean squared error (MSE) between the measured and reconstructed target signals.
The optimal coefficient vector w is obtained by solving the Wiener–Hopf equation, where is the input autocorrelation matrix and is the cross-correlation vector between the inputs and the target.
70% coefficient estimation / 30% testing
Longer history and correct lag compensation both improve reconstruction
Mitigation is strongest at lower frequencies and becomes weaker at high frequencies
Window Size | Lag Offset | SER | Correlation
240 | 8 | 9.77dB | 0.946
240 | 0 | 8.74dB | 0.931
87 | 8 | 8.57dB | 0.928
87 | 0 | 7.60dB | 0.909

## Slide 16: Network and data exchange
SeiMon: ESP32-C3 + ADXL355
MQTT/Wi-Fi measurement streaming
NTP/SNTP time synchronization
SQLite measurement storage
Remote monitoring, commands, and OTA updates
Read-only time, frequency, and statistical analysis
OTA updates completed in less than 30 seconds, with validation and rollback support.

## Slide 17: MEASUREMENT PIPELINE THROUGHPUT
ADXL355 Sampling Rate and MQTT Transmission Test
Configuration | Queue loss
125 Hz, QoS 1 | 0.0%
250 Hz, QoS 1 | 0.0%
500 Hz, QoS 1 | 36.2%
500 Hz, QoS 0 | 0.0%
1000 Hz, QoS 0 | 0.0%
2000 Hz, QoS 0 | 1.9%
500 Hz, QoS 1: unstable, with 36.2% local queue loss and MQTT disconnections
1000 Hz, QoS 0: highest stable tested configuration, with 0% local queue loss
2000 Hz, QoS 0: local throughput limit approached, with 1.9% queue loss
Test conditions and limitations: Tests were performed using a nearby mobile hotspot with strong RSSI values of approximately −23 to −25 dBm. Queue loss was measured locally on the ESP32; broker-side reception and database storage were not verified. End-to-end performance must therefore be evaluated separately in the FZJ network.
Why did QoS 0 help?
QoS 1 requires delivery acknowledgements.

## Slide 18: conclusion
reconstruction is feasible when the witness sensors measure a sufficiently coherent local seismic field.
Performance depends strongly on the target channel, time interval, sensor geometry, and training-data distribution.
ETPF produced the most useful results; Corridonia and most Hi-Net configurations showed weak cross-sensor predictability.
Channel selection can reduce FPGA resources and sometimes improve SER.
Full FPGA integration, inter-node timing accuracy, and end-to-end delivery in the FZJ network remain to be validated.

## Slide 19: Thank you for your attention
Questions? Comments? Advice?
Show me perfect bridge
I said perfect !
Perfection
Georgian-German Science Bridge

## Slide 20: TIMELINE from master thesis proposal
April
March
May
June
Data Processing
Model Development
System Integration
Experimental Validation
Data Analysis
July
August
Write thesis

## Slide 21: background
Seismic activity causes fluctuations in the ground, which generate ground waveforms (seismic waves).
These fluctuations, which introduce seismic noise into the measurement signal.
These density fluctuations generate gravitational forces, which disturb the interferometer mirrors.
This effect, known as Newtonian noise, cannot be shielded or mechanically isolated.
It represents a limitation, especially at low frequencies (see plot).
It must be estimated using external sensors and subtracted from the interferometer signal.
Problem Statement
Projection of displacement sensitivity for the
ETpathfinder operating At 1550 nm laser light and 18 K

## Slide 22: Methodology
There are too many possible combinations
Parameters interact with one another and relationship is not trivial
It takes time to make good evaluation of each model
Hyperparameter optimization
Manual search | Grid search | Random search | Bayesian optimization

## Slide 23: methodology
Correlation
SER
Frequency domain evaluation
Residual analysis
Idealized baseline study
Model performance evaluation
Ratio between target-signal power and residual power, expressed in dB
Primary evaluation metric Higher SER indicates better reconstruction.
Time-domain and frequency-domain metrics are combined because no single metric fully describes reconstruction quality.

## Slide 24: Methodology
Optuna flow
| Pruner and sampler parameters
Study
Define search space
Suggest hyperparameters
Trial
Build model with hyperparameters
Train each epoch
Promising trial?
Prune trial
Store result

## Slide 25: Methodology
Injected ground truth (GT), i.e. target
sensor data, among the input channels
for model testing (upper bound baseline).
Idealized baseline study
CH N+1 | t-w |  | t-3 | t-2 | t-1
CH 1 |  | … |  |  | 
CH 2 |  | … |  |  | 
CH 3 |  | … |  |  | 
 | : |  | : | : | :
CH N |  | … |  |  | 
CH N+1 |  | … |  |  | 
Window Size = w
CNN
t
CH N+1
Surrounding Sensors
(Channel per Axis)
Current Prediction
of Target Sensor

## Slide 26: methodology
Frequency domain evaluation
was estimated using Welch’s method

## Slide 27: Methodology
Abstraction for database generalisation

## Slide 28: Offline results - etpf
Sanity checks - Idealized baseline study
Wiener filter

## Slide 29: Fpga implementation
FLOW TRAINING + INFERENCE
Offline Training (CPU/GPU)
Preprocessing
(FPGA friendly)
Train network
(PyTorch)
Hls4ml/ ONNX
verification
HDL
Neural Network
verification
HDL
Neural Network
Prediction
Sensor data
Sensor data
Sensor data
Sensor data
Sensor data
Offline data
Less than ~1ms
Preprocessing
(FPGA friendly)
Seismo data
Seismo data
…
Inference (FPGA)
deploy

## Slide 30: Offline results - CorRidonia
Reconstruction performance was poor despite testing different models
Low inter-sensor coherence/correlation indicated weak predictability of the target from neighboring sensors
With only the surrounding sensors, SER decreased to approximately 1 dB.
Model A was more tolerant to time shifts because of its longer historical window.
Therefore, Corridonia was not well suited to the spatial waveform-reconstruction task
Event Generalization and Sanity Checks
Spatial reconstruction requires sufficiently correlated witness sensors. A dataset containing multiple simultaneous channels is not automatically suitable.

## Slide 31: Offline results - etpf
Sanity checks - Idealized baseline study
Could not train much longer, see next slide
Wiener filter

## Slide 32: Offline results - etpf
HALL – cleanroom
COR – corridor NAR – noisy area
Train same model on different time slices

## Slide 33: Offline results - etpf
Peak-to-PEAK, Mean, STD - per Ch
Peak-to-peak amplitude and standard deviation increase during working hours, while the channel means remain comparatively stable.
This pattern is consistent with increased daytime activity at the site.

## Slide 34: Offline results - etpf
Same slice different channels
Same 22:00 time interval evaluated for each target channel
Reconstruction performance varies strongly across channels
The primary target channel (red) is among the most difficult to reconstruct
Performance degrades when the test-data distribution differs from the training-data distribution

## Slide 35: Offline results - etpf
Same slice different channels
Same analysis repeated for the 00:00 time slice
The primary target channel (red) reaches approximately 7.3 dB
Reconstruction performance therefore depends on both the target channel and the time-dependent seismic conditions
The negative value indicates unsuccessful reconstruction for one channel

## Slide 36: More questions than answers
So another 8 days
Sharp SER reductions occurred repeatedly and were not unique to the original 20–22 h interval.
Some drops coincided with increased peak-to-peak amplitude and standard deviation, but these statistics did not explain every degradation.

## Slide 37: Offline results - etpf
Peak-to-PEAK, Mean, STD - per Ch

## Slide 38: Offline results – Hi-net
Hi-net provides a large-scale spatial test beyond the local ETPF and Corridonia arrays.
Reconstruction performance is strongly station-dependent: HOT reaches 5.39 dB, while CCH remains near 0 dB.
Large station spacing reduces shared seismic information and introduces propagation delays.
Station geometry and local geological conditions can strongly affect predictability.
DC components were removed before the final evaluation.
HOT was the main successful case; most other evaluated targets remained below approximately 1 dB.
Reconstruction Across Widely Separated Stations
CCH
SER : -0.02
HOT
SER: 5.39
Cross-station reconstruction is possible for some station configurations, but it does not generalize uniformly across the Hi-net network.

## Slide 39: Offline results – Hi-net
Recording divided into 100 evaluation segments
Channel-specific DC offsets remain relatively stable
Statistical distributions differ strongly across stations and axes
These differences may contribute to station-dependent reconstruction performance
Hi-net is not statistically homogeneous: prediction models must handle different amplitude scales, and occasional high-energy transients.

## Slide 40: Wiener — ROBUSTNESS
The noise-injection test demonstrates a strong dependence on the target channel’s temporal autocorrelation.
The comparison with the NN is not fully equivalent: the Wiener filter uses current reference-sensor samples, whereas the NN predicts the next sample using only previous measurements.
Relative SER uncertainty: σrel​=0.11
Sensor | 0.5 h | 1 h | 1.5 h | 2 h | 2.5 h | 3 h | 3.5 h | 4 h | 4.5 h | 5 h
COR_SEIS42 | 7.79 | 7.38 | 7.18 | 6.09 | 7.81 | 7.66 | 8.06 | 8.04 | 7.2 | 7.22
HALL_SEIS44 | 6.98 | 6.6 | 6.52 | 4.54 | 6.75 | 6.67 | 6.94 | 6.48 | 6.07 | 3.88
NAR_SEIS16 | 3.8 | 3.56 | 3.66 | 3.63 | 3.7 | 3.62 | 3.69 | 3.76 | 3.57 | 3.11
SER at Different Time Intervals [dB]

## Slide 41: System architecture
Real-time path : Sensors → MQTT → FPGA
Storage path : Sensors → MQTT → Database
Control path : User interface → MQTT → Sensor nodes
Predictions