## Slide 1
Portable Data Acquisition System
for SiPM-Based Particle Detectors
Presented by-Mariam Titilokashvili
Agricultural University of Georgia
Supervisor- David Mchedlishvili

## Slide 2
What is SiPM
  Highly sensitive semiconductor device
  Detects very weak light signals
  Consists of many small SPAD cells

## Slide 3
SiPM Signal characteristics
Amplitude:~ μA-mA
Rise time:~1ns
Pulse duration:~10-100ns
Requires fast electronics for readout

## Slide 4
How to detect particles with SiPM?
A scintillator is a material that produces photons when a particle deposits energy in it.

## Slide 5
Motivation
Making a low-budget and simple DAQ system for particle detection
Based on locally available hardware components
Portable and compact system

## Slide 6
System Development Approach
Detect and amplify short SiPM signals.
Signal reshaping for slow electronics(mcu)
MCU-based rate counter(and amplitude spectrum)
User interface

## Slide 7
System Overview
SiPM Detector
BJT Preamplifier
Monovibrator
Counting and data representation

## Slide 8
Amplifier circuit
Simulated in NI Multisim
SiPM signal
Preamplifier output

## Slide 9
Monovibrator circuit
Simulated in NI Multisim
<2.52V
2.52V
Signal from preamplifier

## Slide 10
+VCC
VH
VL
+VCC
R6
R5
R1
R6
R3
R5
R1
a
R3

## Slide 11
C1
R2
R7
R4

## Slide 12
Complete circuit

## Slide 13
PCB design
Laser printer;
Iron;
Na peroxide;
Copper board;
Liquid soldering paste;

## Slide 14
Generator test
20Ω
30Ω
Input signal characteristics:
Type: Pulse
Frequency: 100Hz
Amplitude: 10mV
Pulse width: 20ns
Lead edge: 4ns
Trail edge: 4ns
Preamplifier output signal
Monovibrator output signal

## Slide 15
Real test with cosmics
Plastic scintillator
Output signal
Input SiPM signal
Board

## Slide 16
  Implement SiPM signal counting and rate analysis using a microcontroller
  Measure the amplitude of SiPM signals
  Analyze and characterize the detected signals
Future Plans

## Slide 17
Thank You!