## Slide 1
Determining the Movement of an Object Using IMU Sensors
Bachelor project • Embedded IMU system • Real-time inertial measurement and flight-distance estimation
PRESENTED BY
Nikoloz Kurdghelashvili
PROGRAMME / INSTITUTION
[agricultural university of Georgia(AUG)/electrical engineering]
SUPPORTED BY
GGSB

## Slide 2
Why measure the movement of an object?
The project began with a general motion-tracking problem and evolved into a focused, testable measurement task.
WHERE IMUS ARE USED
Inertial sensing is common when direct position measurement is difficult or impractical.
MY MOTIVATION
Build a low-cost embedded system that can observe a thrown object's motion using only onboard inertial sensors.
Robotics and drones
Navigation and motion tracking
Wearable and sports systems
Industrial monitoring
Portable hardware
No external positioning system
Real-time processing on an STM32
Physically measurable output
The goal was not just to read sensors — it was to turn inertial measurements into a meaningful physical quantity.

## Slide 3
What is an IMU?
An Inertial Measurement Unit measures motion using inertial sensors.
Accelerometer
Linear specific force
Measures along X, Y, Z
Gravity is included in the measurement
Gyroscope
Angular velocity
Measures rotation about X, Y, Z
Used to track orientation changes
Sensor fusion
Combine measurements
Orientation helps interpret acceleration
Calibration and filtering reduce error
My IMU
Two sensors + MCU
MMA8452Q accelerometer
MPU6050 gyroscope
STM32F103C8T6 processor

## Slide 4
How an IMU turns motion into data
The sensors do not directly measure position. Position must be reconstructed from measured acceleration and rotation.
1
Measure
2
Estimate orientation
3
Transform
4
Remove gravity
5
Integrate
aₓ, aᵧ,a + ωₓ, ωᵧ, ω Acceleration and angular velocity are sampled over time
Roll and pitch Gyroscope tracks changes. Accelerometer provides gravity reference
Body frame → world frame Rotate acceleration into a fixed coordinate frame
Linear acceleration Subtract the gravity vector after orientation correction
Velocity → position Numerical integration accumulates motion over time

## Slide 5
How an IMU turns motion into data

## Slide 6
Why direct IMU position tracking is difficult
The key problem is not the integral itself — it is the small errors entering the integral.
IDEAL PHYSICS
Acceleration
velocity
position
REAL SENSOR
Bias + noise + orientation error
v(t) = ∫ a(t) dt
x(t) = ∫ v(t) dt
Small acceleration bias creates velocity drift
Orientation error leaks gravity into linear acceleration
Double integration makes position error grow rapidly
The project therefore shifted from full inertial navigation to a constrained flight experiment.

## Slide 7
Why direct IMU position tracking is difficult
The key problem is not the integral itself — it is the small errors entering the integral.
IDEAL PHYSICS
Acceleration
velocity
position
v(t) = ∫ a(t) dt
x(t) = ∫ v(t) dt
The project therefore shifted from full inertial navigation to a constrained flight experiment.

## Slide 8
The project changed because the physics exposed a limitation
The original objective was more ambitious than the available sensing accuracy could support.
INITIAL OBJECTIVE
Real-time 3D position
FINAL OBJECTIVE
Horizontal flight distance
Estimate x, y, z continuously
Start from an arbitrary initial orientation
Use IMU measurements to reconstruct the trajectory
Detect launch and impact
Estimate horizontal velocity
Use measured flight time to calculate traveled distance

## Slide 9
Physics approach

## Slide 10
System hardware
A compact embedded prototype combines inertial sensors, an MCU and a local display.
STM32F103C8T6
Main controller
Runs firmware
Performs calculations
8 MHz system clock in current project
MMA8452Q
3-axis accelerometer
±2 g configuration
Corrected interpretation: 12-bit, 1024 counts/g
MPU6050
3-axis gyroscope
±250 °/s configuration
131 LSB/(°/s) scale in driver
16×2 LCD
Local interface
Shows operating state
Displays velocity, flight time and result

## Slide 11
Built schematic

## Slide 12
Electrical architecture and key interfaces
Derived directly from the STM32CubeMX configuration and firmware.
Function | Device / signal | STM32 pins | Interface / role
Shared IMU bus | MMA8452Q + MPU6050 | PB6 / PB7 | I²C1 SCL / SDA
LCD control | RS / E | PA0 / PA1 | GPIO output
LCD data | D4–D7 | PA4–PA7 | 4-bit parallel GPIO
Reset input | RESET_BTN | PB8 | GPIO input with pull-up

## Slide 13
The mathematical pipeline
This is the core physics-to-computation path used by the project.
1. Calibrate
2. Estimate orientation
3. Rotate acceleration
4. Remove gravity
5. Integrate
Estimate sensor bias Average stationary samples. Gyro zero-rate bias. Accelerometer bias
Roll / pitch Integrate gyro rate. Correct long-term drift with gravity reference
R = R(roll,pitch) Convert body-frame acceleration to world frame
a_linear = a_world − g Gravity is subtracted only after frame transformation
v = ∫a dt Accumulate pre-launch velocity estimate

## Slide 15
Launch and impact become events in a state machine
Instead of trying to reconstruct the full trajectory continuously, the firmware detects key transition events.
IDLE
Waiting
Orientation updated. Monitor acceleration magnitude
PRE-LAUNCH
Acceleration phase
Begin velocity integration. Track body-to-world acceleration
FLIGHT
Free-flight phase
Freeze launch velocity estimate. Measure elapsed flight time
LANDED
Impact detected
Compute distance. Display result. Reset for next test

## Slide 16
Launch and impact become events in a state machine

## Slide 17
Distance estimation uses a deliberately constrained physical model
For a short flight, horizontal acceleration is assumed negligible compared with the launch velocity.
MEASURED / ESTIMATED
From the IMU
PHYSICS MODEL
Projectile motion approximation
Horizontal launch velocity: v_horizontal
Flight time: T = t_impact − t_launch
D = v_horizontal × T
Assumes negligible horizontal air resistance
Assumes launch and impact define the measured flight interval
The simplification reduces the amount of inertial integration required during free flight.

## Slide 18
Building the prototype: from firmware to physical hardware
The system was assembled as a compact throw-test unit with the electronics protected inside an enclosure.
ELECTRICAL BUILD
Wiring and interfaces
MECHANICAL BUILD
Protect the electronics
Shared I²C bus for both IMU devices
4-bit parallel LCD
IMU and controller placed inside a protective box
Designed to survive repeated throwing and impact
Sensor orientation fixed relative to the enclosure

## Slide 19
Building the prototype: from firmware to physical hardware
The system was assembled as a compact throw-test unit with the electronics protected inside an enclosure.

## Slide 20
Testing exposed problems that were invisible on paper
The first working prototype did not behave as the ideal model predicted.
OBSERVED PROBLEMS
During early testing
DEBUGGING APPROACH
Reduce complexity
Very large apparent drift
Free-flight detection did not trigger reliably
Position reconstruction was therefore abandoned
Test raw acceleration first
Compare expected axis response with actual readings
Verify sensor identity and scaling before changing algorithms

## Slide 21
A hardware identification error became a key debugging lesson
The accelerometer driver was initially written for MMA8451Q, but the actual device identified itself differently.
WHAT THE SOFTWARE ASSUMED
MMA8451Q
WHAT THE HARDWARE REPORTED
WHO_AM_I = 0x2A
14-bit interpretation
>> 2 conversion
4096 counts/g
MMA8452Q identity
12-bit output
>> 4 interpretation
1024 counts/g at ±2 g
Correctly identifying the sensor fixed the axis-scaling problem and restored normal acceleration measurements.

## Slide 22
Results table — replace placeholders before presenting
A compact table for comparing measured ground truth with the embedded estimate.
Trial | Actual distance (m) | Calculated distance (m) | Error (%) | Flight time (s)
1 | [_5m__] | [__7.5m_] | [_25%__] | [_3__]
2 | [_10m__] | [_8m__] | [_20%__] | [_6__]
3 | [__15m_] | [__16.7_] | [__11%_] | [_8__]
4 | [__20m_] | [__18.6_] | [__7%_] | [_10__]

## Slide 23
What I gained from the project
The strongest outcome is the ability to move between theory, hardware, firmware and experimental evidence.
1
Physics
Connected projectile motion, gravity and numerical integration to a real measurement problem.
2
Embedded systems
Built an STM32-based sensing system with I²C peripherals, timing and a local user interface.
3
Sensor fusion
Learned why orientation quality controls gravity compensation and therefore velocity accuracy.
4
Experimental method
Learned to isolate faults systematically instead of tuning thresholds blindly.

## Slide 24
Future goals
1
Less errors
With better hardware reduce the error as much as possible
2
Real life usage
To implement this device into real life appliations
3
Return to the original
After making this project better, finish what I started and make 3d navigation

## Slide 25
The main conclusion
The project became stronger when the real engineering limitations were treated as part of the research.
1
The problem
IMU-based movement estimation is fundamentally sensitive to sensor error and orientation.
2
The solution
The original 3D-position objective was reformulated into a constrained flight-distance measurement problem.
3
The lesson
Correct sensor identification, calibration, physics and experimental validation matter as much as the firmware itself.

## Slide 26
Thank you
Questions & discussion
TAKEAWAY
Determining the Movement of an Object Using IMU Sensors