## Slide 1
Nuclear Reactor Dynamics
Simulation Using FPGA
Pavle Erikashvili
Supervisor: Giorgi Macharashvili
Agricultural University of Georgia
GGSB 2026 · Physics session · 8 September 2026
Notes: TIME: 20 seconds. Running time: 0:00–0:20.
SPEAKER NOTES
I am Pavle Erikashvili, from the Agricultural University of Georgia. This project was carried out with Giorgi Macharashvili. I developed a simulator of nuclear-reactor dynamics and implemented its physics model on an FPGA. I will explain the motivation, the physical model, the hardware, and the experiments.
SOURCES
Pavle Erikashvili, original Georgian presentation: პრეზენტაცია.pptx (27 slides).
GGSB_Workshop_2026_Program_FINAL_September.pdf, pp. 4–5: Physics Topics, 8 September 2026, AUG/FUT, Auditorium 314; Pavle Erikashvili (with Macharashvili), AUG.
SOURCE / EDITORIAL NOTES
The supervisor’s full name is taken from the original Georgian title slide. The title has no explanatory or promotional subtitle.

## Slide 2
What’s it all about?
The aim of the project is to create a simplified digital analogue of a small modular pressurized water reactor on an FPGA platform.
The FPGA-based simulator calculates in real time:
Reactor power changes
Fuel and coolant temperatures
Reactivity
Decay heat
Iodine-135 and Xenon-135 dynamics

## Slide 3
Motivation & Georgia’s Energy Context
Reactor Physics Fundamentals
Target Reactor & Mathematical Model
FPGA Implementation
Simulator Architecture & Operation
Experimental Results & Verification
Presentation Overview

## Slide 4
Context
Hydropower output
is seasonal. Solar is intermittent.
Nuclear power is one
option to study for
supply diversification.

## Slide 5
Source: Caucasus Research Resource Centers, Georgia - attitudes towards climate change
Context

## Slide 6
Reactor physics is easier to understand when its dynamics can be seen, not only calculated.
The simulator helps students and the public build an intuitive understanding of:
power increase and decrease
control-rod effects
emergency shutdown - SCRAM
temperature feedback
xenon poisoning
It turns abstract reactor physics into observable behavior.
Making Reactor Physics Intuitive

## Slide 7
Prototype Interface

## Slide 8
Mass Defect

## Slide 9
Chain Reaction

## Slide 10
Chain Reaction
Criticality is a neutron balance
k is the neutron multiplication factor from one generation to the next.
Withdraw rods
Less neutron absorption
Higher reactivity
Insert rods
More neutron absorption
Lower reactivity
k < 1
Subcritical
The chain reaction decreases.
k = 1
Critical
Steady power at equilibrium.
k > 1
Supercritical
The chain reaction grows.
ρ = (k − 1) / k
Reactivity measures departure from criticality.

## Slide 11
Prompt and Delayed Neutrons
Effective delayed fraction
β = 0.007 in this model
Λ = 20 μs
Prompt generation time

## Slide 12
Fuel, moderator and control rods
The neutron balance depends on what each material does.
Fuel
Fission produces heat and new neutrons.
Moderator: water
Slows neutrons, increasing the probability
of U-235 fission.
Control rods
Absorb neutrons; insertion reduces reactivity.
In this reactor type, the same water also removes heat from the fuel.

## Slide 13
Iodine & Xenon
2.65 × 10⁶ b
Thermal absorption cross-section
at 0.0253 eV
Xe-135:
U-235:
585 b

## Slide 14
Reactor Types

## Slide 15
The selected reference model is a small modular pressurized water reactor: PWR-SMR.
PWR: Pressurized Water Reactor
SMR: Small Modular Reactor
Generation III: passive safety features
Coolant: light water (H₂O with deuterium)
Moderator: light water
The reactor core is relatively compact
The model is intended to study the reactor’s overall dynamic behavior
Target Reactor

## Slide 16
Point Kinetics
Pros:
Much lower computational complexity.
Fast enough for real-time simulation
Well suited for studying overall reactor power dynamics
Easy to couple with temperature feedback, xenon, decay heat, and control rods

## Slide 17
Negative Thermal Feedback
Reactor power increases → fuel and coolant temperatures rise.
Higher temperature introduces negative reactivity in the model.
Negative reactivity slows the chain reaction and limits further power increase.
This creates a self-stabilizing feedback loop.
Fuel temperature responds faster than coolant temperature.
In the model, total temperature feedback is the sum of fuel and coolant contributions:
Power ↑ → Temperature ↑ → Reactivity ↓ → Power growth is suppressed.

## Slide 18
Mathematical System and Solver
Stiff Differential Equation System
Numerical Solver
taylor first order approximation:

## Slide 19
Field Programmable Gate Array (FPGA)
FPGA - Field-Programmable Gate Array is a chip whose digital logic can be configured for a specific task.
Unlike a CPU, it does not simply execute a sequence of software instructions; the algorithm is implemented as hardware logic.
This gives predictable and repeatable execution time, which is useful for real-time simulation.
Independent operations can be organized in parallel or pipelined hardware.

## Slide 20
Timestep Comparison
FGPA:
CPU:

## Slide 21
AMD Zynq-7000 AP SoC XC7Z020-CLG484
Dual-core ARM Cortex™-A9 processor
512 MB DDR3
256 MB Quad-SPI Flash
On-board USB-JTAG Programming
10/100/1000 Ethernet
USB OTG 2.0 and USB-UART
Analog Devices ADAU1761 SigmaDSP® Stereo, Low Power, 96 kHz, 24-Bit Audio Codec
Analog Devices ADV7511 High Performance 225 MHz HDMI Transmitter (1080p HDMI, 8-bit VGA, 128x32 OLED)
PS & PL I/O expansion (FMC, Pmod, XADC)
ZedBoard Zynq-7000 ARM/FPGA SoC Board

## Slide 22
Development Flow

## Slide 23
Control Flow

## Slide 24
What the Simulator Does
A real-time, controllable PWR-SMR-like reactor dynamics model running on both PC and FPGA.
Neutron kinetics — reactor power and six delayed-neutron precursor groups
Reactivity & control — control rods, temperature feedback, xenon feedback, and SCRAM
Thermal response — fuel and coolant temperatures, thermal power, and decay heat after shutdown
Iodine–xenon dynamics — I-135/Xe-135 production, decay, neutron absorption, and the post-shutdown xenon peak
Operation & observation — power presets, reset, 1× / 10× / 1000× time modes, telemetry, and graphical monitoring
PC–FPGA comparison — the same physics core runs in software and on the FPGA for direct result comparison

## Slide 25
Results
Mode | Frames | Average time per step | Frame computation time | Achieved time factor | Missed Frame
REALTIME | 1051 | 1.113 μs | 1.113 ms | 1.000856 / 1.000841 | 0
TRAINING | 1051 | 1.113 μs | 1.113 ms | 9.999985 / 10.008559 | 0
XENON | 1050 | 1.110 μs | 55.500 ms | 999.362728 / 1000.304810 | 1
Solver Accuracy compared to RK4
Achieved computation time

## Slide 26
Results
Different plant types comparison

## Slide 27
Results
PC – FPGA Parity

## Slide 28
Results
Decay Heat

## Slide 29
Results
Xenon Worth and Required Critical Rod Position

## Slide 30
Numerical Verification Against CATS
Public benchmarks verified:
CATS Thermal Reactor I, −0.5$ reactivity step, Table 2a Maximum sampled neutron-density error: 0.01599%.
CATS Thermal Reactor I, −1.0$ reactivity step, Table 2b Maximum sampled neutron-density error: 0.02338%.
CATS Thermal Reactor IV, +1$ adiabatic Doppler-feedback transient, Table 6a This is the closed feedback-loop case. Maximum error across 11 published values from 1–100 s: 0.00703%.

## Slide 31
Numerical Verification Against CATS

## Slide 32
Numerical Verification Against CATS

## Slide 33
Demonstration

## Slide 34
Higher dimension reactor model - move beyond point kinetics to spatial neutron-flux and temperature distributions
Hardware-in-the-Loop (HIL) - use the FPGA simulator as a real-time plant model for testing external control systems
Plant-specific validation - calibrate and compare the model against a defined reactor design and published transients
Higher-fidelity thermal hydraulics - add pressure, coolant flow, steam generation, and more detailed heat transfer
Improved iodine-xenon model - more detailed poison dynamics and spatial xenon effects
Expanded control and safety systems - automatic regulation, protection logic, and additional accident scenarios
Scalable FPGA architecture - distribute larger models across more FPGA resources or multiple devices
Future Development

## Slide 35
Github Project
https://github.com/CiyviParturi1/ReactorSim

## Slide 36
Thank You!
Pavle Erikashvili
Supervisor: Giorgi Macharashvili
Agricultural University of Georgia
GGSB 2026 · Physics session · 8 September 2026
Notes: TIME: 20 seconds. Running time: 0:00–0:20.
SPEAKER NOTES
I am Pavle Erikashvili, from the Agricultural University of Georgia. This project was carried out with Giorgi Macharashvili. I developed a simulator of nuclear-reactor dynamics and implemented its physics model on an FPGA. I will explain the motivation, the physical model, the hardware, and the experiments.
SOURCES
Pavle Erikashvili, original Georgian presentation: პრეზენტაცია.pptx (27 slides).
GGSB_Workshop_2026_Program_FINAL_September.pdf, pp. 4–5: Physics Topics, 8 September 2026, AUG/FUT, Auditorium 314; Pavle Erikashvili (with Macharashvili), AUG.
SOURCE / EDITORIAL NOTES
The supervisor’s full name is taken from the original Georgian title slide. The title has no explanatory or promotional subtitle.