## Slide 1
Author: Ina Pipia
ROLE OF FORMIC ACID IN THE ENANTIOSEPARATION OF NEW CHIRAL TELLURONIUM COMPLEXES USING HIGH-PERFORMANCE LIQUID CHROMATOGRAPHY
Supervisor: Academician Bezhan Chankvetadze

## Slide 2: Aim of the study
Achieve HPLC enantioseparation of newly synthesized chiral telluronium complexes.
Compare LGR918 and LGR924, which share the same cation but contain different anions.
Investigate whether the observed species is the intact complex, the common cation, or a formate-associated species.
Evaluate the influence of mobile-phase additives, especially formic acid, on enantioseparation.
LGR918
LGR924
2

## Slide 3
X-ray crystallography analysis of Rac-LGR924
3

## Slide 4
σ-hole
σ-hole
σ-hole
σ-hole
σ-hole
σ-hole
3D molecular model
4
Molecular electrostatic potential surface
Molecular Structure and σ-Hole Representation of the Telluronium Complex

## Slide 5
Mobile Phase: EtOH+0.1%FA
Mobile Phase: EtOH/Hex 30:70 +0.1%FA
Mobile Phase: EtOH/Hex 20:80 +0.1%FA
Effect of Hexane Content on the Enantioseparation
1.9
13.0
16.6
21.8
28.8
1.8
12.9
16.6
21.4
27.5
5
Chromatographic Conditions :
Column-Cellulose-4
Injection Volume: 5mcL
Flow Rate: 1mL/min
Wavelength: 254nm

## Slide 6: Used mobile and stationary phases
Chiral Columns:
Lux-Cellulose-1
Lux-Cellulose-2
Lux-Cellulose-3
Lux-Cellulose-4
Lux-i-Cellulose-2
Lux-i-Cellulose-5
Lux-Amylose-1
Lux-Amylose-2
Lux-Amylose-3
Lux-i-Amylose-3
Mobile Phases:
Hexane : Ethanol (70:30)
Hexane : Ethanol (70:30) +0.1%FA
Hexane : Isopropanol (70:30) +0.1%DEA
Acetonitrile (ACN) +0.1%DEA
Methanol (MeOH) +0.1%DEA
Screening Stage
Chromatographic Conditions :
Injection Volume: 5mcL
Flow Rate: 1mL/min
Wavelength: 254nm
Temperature: C
Mobile Phase Additives:
DEA
NH4OH
Formic Acid (FA)
Ammonium Acetate
6

## Slide 7
Cellulose-2
Cellulose-4
i-Amylose-3
Mobile Phase: Hex/EtOH 70/30+0.1%FA
Formic-acid-dependent enantioseparation
7

## Slide 8
Column: Cellulose-2
Mobile Phase: Hex/EtOH 70/30
Flow Rate: 1mL/min
Wavelenght: 254nm
Inj.Volume: 5mcL
Column: Cellulose-2
Mobile Phase: Hex/EtOH 70/30+0.1%FA
Flow Rate: 1mL/min
Wavelenght: 254nm
Inj.Volume: 5mcL
Spiked Sample
918
Racemate
918
Column: Cellulose-2
Mobile Phase: Hex/EtOH 70/30
Flow Rate: 1mL/min
Wavelenght: 254nm
Inj.Volume: 5mcL
Effect of Prior Formic Acid Exposure on Enantioseparation
Spiked Sample
918
This Analyze was performed before FA being introduced to the column
10.2
12.3
15.3
10.9
13.5
8

## Slide 9
Decrease Of Enantioseparation
Column: Lux-Cellulose-2 | Mobile phase: Hex/EtOH 70/30+ 0.1% FA
The column was washed with isopropanol and methanol to reduce the possible formic-acid-conditioned state.
After switching back to Hexane/Ethanol 70:30 without formic acid, LGR918 was analyzed repeatedly.
Enantioseparation gradually decreased, suggesting that the formic-acid-related column effect was progressively lost.
9
13.0
16.6

## Slide 10
Column: Cellulose-2
Mobile Phase: Hex/EtOH 70/30
Flow Rate: 1mL/min
Wavelenght: 254nm
918
1H
2H
3H
4H
10
16.9
17.8
19.9
13.7
15.3
15.9
16.8

## Slide 11
Low formic-acid concentration: time-dependent restoration
Using 0.00125% FA, the first 918 injection did not reach baseline separation. After 924 was injected, a repeated 918 injection showed improved separation.
918 – 1st injection
924 injection
918 – 2nd injection
11
Chromatographic Conditions:
Column: Cellulose-2
Mobile Phase: Hex/EtOH 70/30+0.00125%FA
Flow Rate: 1mL/min
Wavelenght: 254nm
Inj.Volume: 5mcL
17.6
19.4
14.3
16.9
14.0
16.8

## Slide 12
Restoration Of The Enantioseperation
Column: Cellulose-2
Mobile Phase: Hex/EtOH 70/30
Flow Rate: 1mL/min
Wavelenght: 254nm
Inj.Volume: 5mcL
The column was washed for 0.5 hours in hexane/ethanol (70/30) mobile phase.
• Methanol washing was used to remove the FA-conditioned enantioselective state.
• After washing, Hex/EtOH (70:30) was run and LGR918 was analyzed.
• With longer methanol washing, retention time increased and peak shape broadened.
• After switching to Hex/EtOH + 0.00125% FA, several injections/time were required to restore reproducible separation.
12
19.8

## Slide 13
Chromatographic Conditions:
Column: Cellulose-2
Mobile Phase: Hex/EtOH 70/30+0.00125%FA
Flow Rate: 1mL/min
Wavelenght: 254nm
Inj.Volume: 5mcL
Restoration of enantioseparation with 0.00125% formic acid
13
23.8
18.1
19.4
14.9
17.2
14.1
16.8
14.1
16.8

## Slide 14
924 I
924 II
CD spectra of enantiomeric fractions
CD gives chiral information beyond UV-DAD
14
918 I
918 II

## Slide 15
918 ACN
Agilent Technologies Cary 60 UV-VIS
918 ACN+FA
924 ACN+FA
Effect of Formic Acid on UV-Visible Spectra
924 ACN
Does the presence of formic acid alter the UV-visible absorption profile of LGR918 and LGR924?
16

## Slide 16
BArF
UV-Vis Analysis of LGR918 and LGR924 Conducted in Strasbourg
17

## Slide 17
HPLC-DAD Analysis of LGR918 with Formic Acid
19
918
New Cellulose-2 Column
Hex/EtOH 70/30 + 0.1% FA

## Slide 18
918
New Cellulose-2 Column
Hex/EtOH 70/30
HPLC-DAD Analysis of LGR918 without Formic Acid
18

## Slide 19
• The optimal enantioselective separation was achieved on a cellulose-based chiral column under normal-phase conditions using Hex/EtOH with formic acid.
• Formic acid plays an important role in the separation, although column conditioning and residual acid effects may also influence the chromatographic behavior.
• UV and HPLC-DAD spectra of LGR918 and LGR924 were similar, suggesting that the main UV-active species is associated with the common chiral telluronium cation.
Current Interpretation
20

## Slide 20
Thank you for your attention!