## Slide 1
ENVIRONMENTAL RESEARCH
Environmental Quality Assessment of Soils and Waters
Through Heavy Metal Analysis Using MP-AES: A Case Study from Selected Areas of Western Georgia
Researchers:
Ana Gabedava & Nino Takaishvili

## Slide 2
02
Research Aim and Context
Two Related Environmental Datasets
Water
Soil
Analysis
Physicochemical parameters, heavy metals, and major elements
2
Main Objective
Assessment of the main chemical parameters of soils and waters in Ozurgeti Municipality and identification of elements of concern
10 soil samples from Ozurgeti Municipality, collected from different locations and 0–30 / 30–60 cm layers
10 water samples from Ozurgeti Municipality — river, spring, well, and sulfur water

## Slide 3
03
3
Agilent 4210 MP-AES
The analytical core of the study
Microwave Plasma–Atomic Emission Spectroscopy
Why it matters in this study
Multi-Element quantitative analysis
Safety
Simplicity
High sensitivity
Environmental samples → quantitative elemental data

## Slide 4
04
Spatial Overview of Soil Samples
Sample locations, depth and sampling time
№ | Location | Depth | Date
1 | Ozurgeti, vegetable garden | 0–30 cm | 2025 May
2 | Ozurgeti, vegetable garden | 30–60 cm | 2025 March
3 | Ozurgeti, cornfield | 0–30 cm | 2025 March
4 | Ozurgeti, cornfield | 30–60 cm | 2025 March
5 | Ozurgeti, Hazelnut orchard | 0–30 cm | 2025 March
6 | Ozurgeti, Hazelnut orchard | 30–60 cm | 2025 March
7 | Village Meria, Hazelnut orchard | 0–30 cm | 2025 March
8 | Village Meria, Hazelnut orchard | 30–60 cm | 2025 March
9 | Village Likhаuri, Citrus orchard | 0–30 cm | 2025 March
10 | Village Likhаuri, Citrus orchard | 30–60 cm | 2025 March
4
10 samples • 5 main locations • two depth layers

## Slide 5
05
Moisture, pH and CaCO3
№ | Moisture % | pH | CaCO3 mg/g
1 | 8.90 | 6.90 | 14.40
2 | 9.45 | 6.65 | 12.20
3 | 8.17 | 6.57 | 10.30
4 | 9.13 | 6.52 | 10.70
5 | 7.94 | 6.48 | 10.90
6 | 7.95 | 6.65 | 12.10
7 | 5.32 | 6.75 | 8.70
8 | 5.45 | 6.54 | 10.10
9 | 7.75 | 6.83 | —
10 | 6.91 | 6.53 | 10.00
Mean pH
6.64
Mean moisture
7.70 %
pH range
6.48–6.90
CaCO3
1.0-1.4 %
5
Soil Parameters

## Slide 6
06
Soil pH
Comparison of pH among samples
6
Interpretation: slightly acidic / nearly neutral reaction
pH ranges from 6.5–6.9 in all samples

## Slide 7
07
Variation in moisture among samples
OZURGETI • ENVIRONMENTAL RESEARCH
7
Soil Moisture
Maximum: Sample 2 — 9.45 %
Minimum: Sample 7 — 5.32 %

## Slide 8
08
MP-AES analysis results, mg/kg, g/kg
8
№ | mg/kg |  |  |  |  |  |  |  | g/kg
 | Cd | Pb | Zn | Cu | Ni | Cr | Sb | Mn | Fe
1 | * | 47.00 | 194.9 | 177 | 5.00 | 112 | 69 | 1117 | 75.10
2 | 1.00 | 16.00 | 150.2 | 116 | 10.00 | 115 | 78 | 984 | 78.50
3 | * | 56.00 | 125.7 | 66 | 6.00 | 114 | 69 | 939 | 79.70
4 | * | * | 107.6 | 65 | 9.00 | 132 | 76 | 990 | 82.00
5 | * | 16.00 | 143.0 | 75 | 8.00 | 112 | 63 | 1047 | 82.30
6 | 1.00 | * | 101.0 | 56 | 12.00 | 121 | 76 | 945 | 90.40
7 | * | * | 86.10 | 57 | * | 125 | 53 | 642 | 95.40
8 | * | * | 76.60 | 53 | * | 120 | 66 | 753 | 90.90
9 | 1.00 | * | 131.6 | 105 | * | 115 | 49 | 850 | 91.50
10 | 1.00 | * | 84.60 | 72 | * | 89 | 62 | 580 | 42.50
MPC (pH<7) | 1-1.5 | 50 | 150-200 | 150 | 100 | 65 | 4 | 2500 | 
PLC (pH>6.5) | 0.4-0.5 | 40-50 | 80-150 | 60-80 | 60-80 | 50-60 | 2-4 | 1200-1300 | 
Heavy Metals in Soil
* < DL (Below Detection Limit)

## Slide 9
09
One of the most notable indicators in the soil dataset
Highest value
132 mg/kg
sample 4
9
Mean
115.5 mg/kg
Minimum
89.0 mg/kg
sample 10
Spatial Variation of Chromium (Cr)

## Slide 10
10
10
KEY
Location | Sb in soil mg/kg | Sb in water mg/L
Likhаuri | 49 (0–30 cm) 62 (30–60 cm) | 0.15
Meria | 53 (0–30 cm) 66 (30–60 cm) | 0.08
Ozurgeti | 63 (0–30 cm) 78 (30–60 cm) | 0.10
KEY FINDING
49-78 mg/kg
Antimony (Sb) — One of the Main Findings of the Study
Exceedance: 12–20 times the MPC

## Slide 11
11
Li, K, Na, Ca and Mg — quantitative comparison
№ | mg/kg |  |  |  | 
 | Li | K | Na | Ca | Mg
1 | 9 | 3547 | 3120 | 4709 | 9142
2 | 12 | 3422 | 1900 | 989 | 5104
3 | 14 | 3635 | 2330 | 870 | 4809
4 | 8 | 3262 | 2610 | 2795 | 10259
5 | 9 | 3288 | 1940 | 3512 | 10479
6 | 9 | 3215 | 1980 | 3308 | 9673
7 | 7 | 2929 | 2070 | 3378 | 9895
8 | 8 | 3025 | 2140 | 2754 | 10519
9 | 9 | 3764 | 1860 | 2741 | 10571
10 | 8 | 3622 | 1490 | 2727 | 10562
11
Major Elements in Soil
Ca and Mg values show particularly pronounced differences among samples

## Slide 12
12
Main conclusions from the numerical data
12
01
pH
6.5–6.9
02
Moisture
5.32–9.45 %
03
Cr
04
Fe
05
Sb
Range 4.2-9.5 %
Key Findings from Soil Analysis
Slightly higher in some deeper layers
High concentration, mean 115 mg/kg
High mass concentration
Exceedance: 12–20 times the MPC

## Slide 13
13
Different types of water in Ozurgeti Municipality
№ | Water type | Date
1 | Village Likhаuri, Achi River | 31.10.2025
2 | Village Konkchati, spring water | 31.10.2025
3 | Village Vakijvari, well water | 31.10.2025
4 | Village Silauri, spring water | 31.10.2025
5 | Village Tkhinvali, sulfur water | 31.10.2025
6 | Village Chanieti, well water | 31.10.2025
7 | Village Bakhvi, well water | 31.10.2025
8 | Village Makvaneti, spring water | 02.11.2025
9 | Village Meria, spring water | 31.10.2025
10 | City Ozurgeti, well water | 01.11.2025
River • Spring • Well • Sulfur water
13
Water Samples

## Slide 14
14
pH, total and temporary hardness
№ | pH | Total hardness mg-eq/L | Temporary hardness mg-eq/L | Class
1 | 7.68 | 0.63 | 0.56 | Soft
2 | 7.21 | 4.08 | 3.72 | Hard
3 | 6.81 | 0.71 | 0.76 | Soft
4 | 7.52 | 5.0 | 2.6 | Hard
5 | 7.75 | 0.43 | 0.96 | Soft
6 | 6.11 | 0.38 | 0.32 | Soft
7 | 5.82 | 0.36 | 0.36 | Soft
8 | 6.28 | 0.31 | 0.32 | Soft
9 | 6.71 | 1.4 | 1.44 | Soft
10 | 7.0 | 0.99 | 0.64 | Soft
MPC | 6-9 | 7-10 | - | 
Soft water: 8 / 10 sample
Hard water: 2 / 10 sample
14
Mean pH 6.89
Key Water Parameters

## Slide 15
15
Water pH Profile
Comparison of acid-base reaction among samples
15
Minimum pH: 5.82 (Sample 7) • Maximum pH: 7.75 (Sample 5)

## Slide 16
16
Total Water Hardness
Comparison of hardness values across all samples
16
Highest total hardness: 5.00 mg-eq/L — Sample 4

## Slide 17
17
Comparison of oxidation values among water samples
17
Permanganate Oxidation
All samples are below the MPC of 3.0 mg O₂/L.

## Slide 18
18
Heavy Metals in Water
MP-AES — complete concentration table
№ | mg/L |  |  |  |  |  |  |  |  | 
 | Cd | Pb | Zn | Cr | Cu | Mn | Fe | Sb | Co | Ni
1 | * | * | * | * | * | * | 0.03 | 0.15 | 0.01 | *
2 | * | 0.03 | * | * | 0.01 | * | 0.08 | 0.16 | 0.03 | 0.02
3 | * | * | * | * | 0.01 | * | 0.02 | 0.13 | 0.03 | *
4 | * | 0.01 | * | * | 0.01 | * | 0.02 | 0.07 | 0.01 | 0.01
5 | * | 0.03 | * | * | 0.01 | * | 0.04 | 0.15 | 0.01 | 0.01
6 | * | * | * | * | * | 0.09 | 0.04 | 0.11 | 0.02 | 0.01
7 | * | * | 0.01 | * | 0.01 | 0.03 | 0.42 | 0.10 | 0.02 | 0.01
8 | * | * | * | * | 0.01 | 0.01 | 0.11 | 0.09 | 0.03 | 0.01
9 | * | * | * | * | 0.01 | * | 0.03 | 0.08 | 0.02 | 0.01
10 | * | * | * | * | 0.01 | * | 0.04 | 0.10 | 0.03 | *
MPC | 0.003 | 0.01 | 3 | 0.05 | 1 | 0.5 | 0.3 | 0.02 | - | 0.02
WHO | 0.003 | 0.01 | 3 | 0.05 | 2 | 0.08 | 0.3 | - | - | 0.07
18
* < DL (Below Detection Limit)

## Slide 19
19
The most notable quantitative difference among samples
19
3x Exceedance:
sample: 2, 5
In Sample No. 4, the value is exactly at the limit, while lead was not detected at the other 7 locations
lead (Pb) Concentration in Water

## Slide 20
20
K+, Na +, Ca²⁺ and Mg²⁺ — an integrated chemical profile
a | mg/L |  |  | 
 | K+ | Na+ | Ca²+ | Mg²+
1 | 0.61 | 2.92 | 6.20 | 3.20
2 | 1.68 | 7.81 | 79.20 | 0.30
3 | 0.78 | 2.46 | 16.00 | -0.90
4 | 1.48 | 14.28 | 40.00 | 7.50
5 | 1.31 | — | 7.4 | 0.60
6 | 3.70 | 4.10 | 6.80 | 0.40
7 | 2.35 | 3.30 | 4.40 | 1.40
8 | 3.68 | 5.58 | 2.40 | 1.90
9 | 0.44 | 4.95 | 18.20 | 4.90
10 | 7.41 | 5.91 | 14.00 | 2.90
20
Major Ions in Water
Sample 2 is notable for its high Ca²⁺ value — 79.2 mg/L.
Maximum Na: 14.28 mg/L

## Slide 21
21
Combined interpretation of soil and water data
20
01
Soil
02
Water
pH (6.5–6.9) and CaCO₃ (10–14 mg/g) are consistent with a normal, slightly acidic / neutral environment
Iron (Fe: 42.5–95.4 g/kg) and chromium (Cr: 115 mg/kg) concentrations are high, but remain within natural background variation
(Sb): Antimony in soil reaches 49–78 mg/kg, significantly exceeding the maximum permissible concentration (MPC). Potential Origins: Natural geochemical background, long-term environmental accumulation, or anthropogenic impact.
80% of the samples are soft, and permanganate oxidation is within the normal range at all locations (< 3.0 mg O₂/L).
(Pb): At 2 locations (village of Konchkati and Tkhinvali), the lead concentration is 0.03 mg/L, which is 3 times higher than the limit (0.01 mg/L)
Integrated Conclusion
Overall: targeted monitoring is recommended

## Slide 22
Thank you
for your attention!