## Slide 1: First Baseline Separation of Isotopomers by Capillary Electrophoresis
Prepared by: Nikoloz Gonitashvili
Ivane Javakhishvili Tbilisi State University
Supervisor: Academician Bezhan Chankvetadze

## Slide 2: Research Relevance and Methodological Novelty
Isotopomers in modern analysis – The significance of structural isotope effects for the precise molecular identification of substances.
Key application areas – Isotopic purity control, the study of weak non-covalent interactions, and the in-depth analysis of pharmaceutical preparations.
Research novelty – The first baseline electrokinetic separation of isotopomers: Utilizing minimal differences induced by the specific positioning of deuterium within the molecule.

## Slide 3: Research Goals and Objectives
Investigation of the first baseline electrokinetic separation of isotopomers in capillary electrophoresis
Optimization of the separation environment: selecting the ideal pH range, buffer composition, and evaluating the impact of chiral/achiral additives.

## Slide 4: ISOTOPOMERS

## Slide 5: Capillary Electrophoresis Instrumentation
Agilent 7100 Capillary Electrophoresis with Diode-Array Detector (DAD)

## Slide 6: Experimental Section
Capillary Electrophoresis Parameters:
  Capillary: Bare fused-silica; 50 μm I.D., 375 μm O.D.
  Length: 98.5 cm total length (90 cm effective length).
  Temperature: 15 °C.
  Voltage: +30 kV (Current: 65–70 μA).
  Injection: Electrokinetic injection (30 kV for 10 s).
  Detection: UV detection at 210 nm.
Capillary Conditioning (Flushing):
  Methanol – 10 min
  Water – 5 min
  0.1 M NaOH – 10 min
  Water – 5 min
  Separation Buffer – 15 min
  Flushing Pressure: 1000 mbar.
Optimized Buffer for Isotomers : 50 mM CHES buffer (pH 11.0).

## Slide 7: First Baseline Separation
Experimental Breakthrough: Achievement of complete baseline resolution (
Separation Mechanism: The differentiation is based on position-specific isotope effects, leveraging minute shifts in values (approximately 0.01 units).
Method Efficiency:
  High Performance: Separation efficiency exceeding 310,000 theoretical plates per meter.
  Migration Profile: Clear temporal distinction with migration times of 21.64 min (aliphatic) and 22.45 min (aromatic).
Optimized System: The separation was finalized using a 50 mM CHES buffer at pH 11.0, utilizing TMA -
Conclusion: This demonstrates the superior sensitivity of capillary electrophoresis in distinguishing between species based solely on the internal localization of isotopes.

## Slide 8: The Role of in the Separation Mechanism
The separation of isotopomers is driven by minute induced by position-specific deuterium substitution.
Deuterium atoms located on the aromatic ring increase basicity more significantly than those on the aliphatic chain, resulting in distinct migration profiles.
This isotopic shift is effectively leveraged at an optimal pH of 11.0, where partial deprotonation creates the necessary difference in effective mobility.

## Slide 9: Electrophoretic separation of AMP and MET isotopomers
The capillary electrophoresis method provides sensitivity to differences (0.01 units) comparable to advanced NMR spectroscopy, but requires one to two orders of magnitude less sample

## Slide 10: Conclusions
First Demonstration: The study provides the first-ever baseline separation of isotopomers based on an electrokinetic migration mechanism.
Structural Insight: It is proven that the isotope effect on depends directly on the molecular position of the deuterium substitution.
High Performance: Separation efficiency exceeded 300,000 theoretical plates per meter, ensuring high resolution.
Future Impact: This method serves as a powerful tool for pharmaceutical analysis, forensic toxicology, and the study of fundamental non-covalent interactions.

## Slide 11: Thank you for your attention