## Slide 1: Minimization of thermo-mechanical influences on the image quality of satellite optical systems
04.09.2026
INSTITUTE OF TECHNOLOGY AND Engineering
GIORGI KAKABADZE
Notes: The upper atmosphere contains valuable information about Earth's climate and allows early detection of changes,
but space environment can significantly affect on-orbit systems,
therefore, before trusting atmospheric measurement, precision of spaceborne instrumentation must be ensured.

## Slide 2: How I appeared in Jülich

## Slide 3: Observe atmosphere
Limb
Nadir

## Slide 4: SHIPAS
Spatial Heterodyne Interferometer Performance Assessment in Space
BAFFLE
FRONT OPTICS
DETECTOR OPTICS
DETECTOR
SPATIAL HETERODYNE INTERFEROMETER
Beamsplitter
Grating
Prism
Prism
Spacer
Final Image on Detector
Notes: Small device with no moving parts,
purpose of baffle (straylight and albido),
Interference explained.

## Slide 5: Orbital Environment
Low Earth Orbit
Orbital period around 90 minutes
Minimum temperature
Maximum temperature
Four critical thermal cases

## Slide 6: What happens to the System?
Animation was created by the assistance of OpenAI

## Slide 7: Structural-thermal-optical-performance
STOP Analysis Workflow
Temperature Fields
Detector image
Structural Displacements
Thermal Analysis
Structural Analysis
Optical Ray Tracing
no
yes
Motion Monitoring Tool
Sufficient Image Quality?
Design
Final Design
Improvement
Temperature, °C
38.8
12.6
Deiml, M. (2017). Development of a small satellite remote sensing payload for passive limb sounding of the atmospheric oxygen emission. Ph.D. dissertation, Universitätsbibliothek Wuppertal.
Final Image on Detector
Displacement, mm
0.12
0.04

## Slide 8: Motion Monitoring Tool
Axial Displacements
Rotation
Scaling
Asymmetric deformation
Example: Lens 1 of SHIPAS for isothermal case
Remaining displacements after subtracting
a) rigid body displacement
max. 13.3 μm
b) rigid body rotation
max. 11.1 μm
c) thermal expansion
max. 4.7 μm

## Slide 9: Analytical validation
Peak | 1 | 2 | 3 | 4
analytical y=0 | -8.075 | -2.052 | 2.052 | 8.075
simulation y=0 | -8.076 | -2.056 | 2.056 | 8.076
analytical y=5 | -7.62 | -3.068 | 2.946 | 7.05
simulation y=5 | -7.625 | -3.069 | 2.95 | 7.056
simulation y=0mm
simulation y=5mm
simulation y=0mm
simulation y=5mm
analytical (python) y=0mm
analytical (python) y=5mm
x [mm]
x [mm]
incoming ray
incoming ray
Detector
-20 -10 0 10 20 30
-20 -10 0 10 20 30
Detector
Notes: Mention that analytical tool was programmed by me

## Slide 10: Point Source Analysis
Preparing simulations for validation
Lens 1 Y + 1 mm
Lens 1 X + 1 deg
Grating 1 X + 1 deg
Lens 5 Z + 1 mm

## Slide 11: Fringe degradation due to Grating tilt
Postprocessing tool to recover fringes from Ntokas (2023)
Origin of the problem in SHI

## Slide 12: Full system analysis
2.7 billion rays
Covering central line segment of the detector
This method is enough for fringe degradation monitoring

## Slide 13: Current status
Interdisciplinary modelling
Thermal model
Structural model
Optical model

## Slide 14: Further steps
Preparing the Experiment
Create experimental setup
Validate numerical model
Analyze detector picture after deformation
Identify critical optical elements
Provide STOP based design suggestions
SHI mounting tool
experimental setup

## Slide 15: Conclusion
Scientific Contribution
STOP workflow development
Commercial software based
Identify main contributors in image degradation
Provide future design recommendations

## Slide 16: Thank you for your attention